## Slide 1
BGP Implementation and IP Header
Lecture 9 (Routing 6)
Slides credit: CS 168 @ UC Berkeley
Notes: Slides template credit: Josh Hug, Lisa Yan
Last routing lecture! Last lecture with midterm material

## Slide 2: External BGP and Internal BGP
BGP Implementation
External BGP and Internal BGP
Multiple Links Between ASes
Message Types and Route Attributes
Issues with BGP
IP Header
IPv4 Header Fields
IPv6 Changes
Security
Lecture 9, Spring 2026
Notes: we'll be
0:02
discussing bgp implementation and the IP
0:05
header so it's a two-part lecture let's
0:08
start by talking about how bgp is
0:10
actually
0:12
implemented so far we've talked about
0:15
bgp at a conceptual level and we've
0:17
thought about the autonomous system as a
0:20
single unit and it talks with other as's

## Slide 3: Combining Intra-Domain and Inter-Domain Routing
So far, we've shown BGP in terms of ASes talking to each other.
An AS advertises routes to its neighbor ASes.
AS#5
AS#4
AS#3
AS#2
AS#1
Notes: so far you've seen graphs like this
0:25
where as's talk to other as's and they
0:29
exchange routes between each other
0:31
however as we know the internet is
0:34
really a network of networks so what
0:37
that means is within each as there's
0:39
actually all these different routers and
0:42
our goal today when implementing bgp is
0:45
to figure out what these routers do so
0:47
that they all act as one single unit so
0:51
in our conceptual picture the as was
0:53
just a single unit and it thought for
0:56
itself and made some decisions

## Slide 4: Combining Intra-Domain and Inter-Domain Routing
In reality, an AS is made up of a bunch of routers.
We have to ensure the routers "act as one."
Today, we'll also see how BGP interacts with intra-domain routing.
B
D
A
G
AS#1
C
E
F
AS#5
AS#4
AS#3
AS#2
Notes: and today
0:59
we will see how all of these routers
1:01
actually work together to act as a
1:03
single brain doing the things that this
1:06
as needs to do exchanging routes
1:08
exporting them importing them so our
1:11
goal is to get all of these routers to
1:13
coordinate with each other in some way
1:15
so that they all act as one single brain
1:18
when it comes to bgp and interdomain
1:22
routing we're also going to see how bgp
1:25
combines with intra domain routing and
1:27
those are the protocols like distance
1:29
vector and Link State and when you
1:31
combine both of those protocols we'll be
1:34
able to find routes to any destination
1:36
in the entire internet

## Slide 5: Border Routers and Interior Routers
Border routers: At least one link to a router in a different AS. (A, B, G)
Interior routers: Only linked to other routers in the same AS. (C, D, E, F)
B
D
A
G
AS#1
C
E
F
AS#5
AS#4
AS#3
AS#2
Notes: so before we get started let's go
1:44
through some terms one term that you'll
1:46
see is a border router these are the
1:49
routers that have links to other
1:51
autonomous systems so in this picture
1:54
routers a B and G are border routers
1:57
because they have links to routers in
2:00
other autonomous systems by contrast an
2:03
interior router is only linked to other
2:06
routers inside the same as so in this
2:09
picture c d e and f are the interior
2:13
routers because they do not have links
2:16
to outside and other as's

## Slide 6: Border Routers and Interior Routers
BGP speakers: The routers that advertise BGP paths to other ASes.
Who speaks BGP? All the border routers inside each AS.
Speakers must understand BGP syntax and semantics.
B
D
A
G
AS#1
C
E
F
AS#5
AS#4
AS#3
AS#2
Notes: The RFC for BGP is here if you're curious: https://datatracker.ietf.org/doc/html/rfc4271
another term that you'll see
2:25
throughout today is bgp Speaker you can
2:29
think of the GP speakers as the routers
2:32
that are speaking on behalf of the
2:34
current as and advertising paths to
2:37
other as's so remember the goal is to
2:40
have all of these routers work together
2:42
as a single unit and the way that they
2:44
will do that is routers a B and G will
2:48
be the bgp speakers and they will talk
2:51
on behalf of as number one sending out
2:54
advertisements and receiving
2:56
advertisements from the neighboring as's
3:03
the bgp speakers need to also understand
3:06
the bgp protocol we have to add extra
3:09
code inside of these routers so that
3:12
they understand how to exchange routes
3:14
with other
3:16
as's so in summary the bgp speakers are
3:20
the Border routers inside each

## Slide 7: Border Routers and Interior Routers
Stub AS
BGP speakers: The routers that advertise BGP paths to other ASes.
Recall: Stub ASes don't need to speak BGP.
The border router can default-route everything to the provider AS.
A
Provider AS
Notes: The RFC for BGP is here if you're curious: https://datatracker.ietf.org/doc/html/rfc4271
one note that you might have already
3:27
seen from the last lecture but we want
3:28
to mention it one more time is that the
3:31
stub as is an as that only has a single
3:34
provider it's kind of like the as
3:36
equivalent of a host in intra domain
3:40
routing so remember when we talked about
3:42
routing inside of a network we said that
3:44
hosts don't participate in routing they
3:47
simply send packets to their next top
3:49
router and the next top router handles
3:51
the packet for them well similarly if
3:54
you have a stub as the stub as doesn't
3:56
have to participate in routing it
3:58
doesn't have to learn any paths or
4:00
exchange any advertisements it simply
4:03
sends every packet that it wants to send
4:06
to its one and only provider and the
4:08
provider does all the work for them so
4:10
as a result the stub as's don't have to
4:13
speak bgp they don't have to participate
4:15
in the routing protocol all that they
4:18
have to do is send all packets to their
4:20
one and only provider as a default route
4:23
and they're all done

## Slide 8: External BGP, Internal BGP, and IGP
B
D
A
G
AS#1
C
E
F
BGP session: Two routers exchanging BGP information between each other.
AS#5
AS#4
AS#3
AS#2
Z
Notes: The RFC for BGP is here if you're curious: https://datatracker.ietf.org/doc/html/rfc4271
bgp session a
4:39
bgp session is a longlived connection
4:42
between two routers that will want to
4:44
exchange bgp information between each
4:47
other any two routers can form a bgp
4:50
session and that will be a longlived
4:53
connection where they can exchange lots
4:55
of information about routes
4:57
advertisements anything like that
5:00
bgp sessions can be formed between
5:02
adjacent routers so for example A and C
5:05
might form a longlived bgp connection
5:08
where they send packets between each
5:09
other but you can also form bgp sessions
5:12
between routers that are further away so
5:15
for example A and G could form a bgp
5:18
session they would forward packets back
5:20
and forth between each other and it's
5:22
true that the packets would have to take
5:24
multiple hops to get from a to G but
5:27
ultimately that is still a bgp session
5:30
so think of it like a long lift
5:31
connection sort of like the connections
5:34
at layers 4 and seven but instead of
5:36
sending user data they are sending bgp
5:40
information

## Slide 9: External BGP, Internal BGP, and IGP
B
D
A
G
AS#1
C
E
F
External BGP (eBGP) session: Between two routers in different ASes.
Border routers use eBGP to exchange inter-domain routes.
AS#5
AS#4
AS#3
AS#2
Z
Hi AS#1. Did you know you can reach Z via AS#5?
Notes: The RFC for BGP is here if you're curious: https://datatracker.ietf.org/doc/html/rfc4271
to actually implement bgp we are
0:03
going to need two types of sessions and
0:06
these two sessions together will help us
0:08
ensure that all of these routers
0:10
coordinate to give the illusion that as
0:13
number one is working as a single brain
0:16
even though it's made up of lots of
0:18
separate routers the first type of bgp
0:20
session is called external bgp session
0:24
and these are the sessions where routers
0:26
in different as's exchange paths between
0:29
each other so the arrows in blue
0:31
represent external bgp sessions for
0:34
example there might be a session between
0:36
G and some router in as number five
0:40
they're talking to each other across two
0:43
different as's and they're exchanging
0:45
routes between each other

## Slide 10: External BGP, Internal BGP, and IGP
Internal BGP (iBGP) session: Between two routers in the same AS.
Border routers use iBGP to distribute the routes it discovers to everyone else in the AS.
B
D
A
G
AS#1
C
E
F
AS#5
AS#4
AS#3
AS#2
Z
Hey everyone, I just found a way to reach Z.
Notes: The RFC for BGP is here if you're curious: https://datatracker.ietf.org/doc/html/rfc4271
if only G knows about the
1:23
path to Z that is not enough because
1:26
remember there are all these routers
1:28
inside as number one one and we want
1:31
them to act as one cohesive unit so what
1:34
that means is if G learns a piece of
1:36
information in order for everyone to act
1:39
as one cohesive unit G needs to share
1:42
the information with the class it needs
1:44
to stand up and tell everyone else in as
1:47
number one hey everyone I just found a
1:49
way to reach G sorry I found a way to
1:52
reach Z that's what G says and so if G
1:55
stands up and announces this information
1:58
to everyone now everyone in the as also
2:01
knows about the way to reach Z and all
2:03
of them are working in sync so in order
2:06
for everyone to be coherent and cohesive
2:10
when someone learns about a path to
2:12
another as they need to stand up and
2:14
announce it to the rest of the class and
2:16
the way that we do that is using
2:18
internal bgp or ibgp sessions these are
2:23
sessions that happen between two routers
2:25
in the same autonomous system and these
2:28
allow the Border routers to distribute
2:30
the routes that they have learned to
2:32
everyone else inside the as so you use
2:36
ebgp for the Border routers to learn the
2:38
route and then you use ibgp to announce
2:42
your findings to the whole class so that
2:44
everyone inside the as is working as one
2:48
cohesive
2:50
unit so those are the two types of bgp
2:53
sessions that can be formed

## Slide 11: External BGP, Internal BGP, and IGP
B
D
A
G
AS#1
C
E
F
Interior gateway protocol: Between two routers in the same AS.
Used to find paths inside the AS (e.g. distance-vector, link-state).
AS#5
AS#4
AS#3
AS#2
Z
Notes: The RFC for BGP is here if you're curious: https://datatracker.ietf.org/doc/html/rfc4271
be careful
2:56
not to confuse them with igp because
2:59
because igp is the interior Gateway
3:02
protocol these are the ones that allow
3:04
you to find paths inside of the as so
3:08
remember when we talked about distance
3:09
vector and Link State protocols those
3:12
were igp protocols they allow you to
3:15
find paths inside of the network so here
3:19
we're drawing the arrows in red to
3:21
denote that these are the routing
3:22
advertisements that would get exchanged
3:24
so that you learn paths inside of your
3:26
network so bgp was used to learn paths
3:30
outside of the network and igp is used
3:33
to learn paths inside of the network
3:36
that distinction still applies

## Slide 12: External BGP, Internal BGP, and IGP
Three types of communications between routers:
eBGP: Routers in different ASes exchanging routes.
iBGP: Router distributing externally-learned routes to interior routers.
IGP: Intra-domain routing protocols for internal reachability.
Be careful not to confuse iBGP and IGP.
Both are between interior routers.
iBGP is for external routes, and IGP is for internal routes.
A
B
Routing protocols
Inter-domain
Intra-domain
eBGP
iBGP
IGP
iBGP: "I can reach AS#5 via [AS#7, AS#9]."
IGP: "I can reach C with cost 3."
Notes: 3:39
all of the pieces together we have a
3:41
taxonomy that looks something like this
3:43
there are two types of routing protocols
3:45
there's the interdomain protocol for
3:48
finding external routes and the int
3:50
domain protocol for finding internal
3:53
routes the intro domain protocol that's
3:55
igp that's distance Vector link state
3:59
that allows you to find the next Toops
4:01
inside of the current Network and the
4:05
inter domain protocol is bgp for finding
4:07
routes outside of the network and that
4:10
consists of two parts ebgp for the
4:13
Border routers to learn the routes and
4:15
then ibgp to distribute those routes

## Slide 13: Combining Intra-Domain and Inter-Domain Routing
1. Use IGP to learn internal routes to others in the AS.
B
D
A
G
AS#1
C
E
F
AS#5
AS#4
AS#3
AS#2
1. To reach G, my next-hop is F.
Z
Notes: let's look at how you
0:11
use all three of them together to
0:13
combine intra domain and Inter domain
0:16
routing to achieve paths to every
0:19
destination internal or external now do
0:23
remember that routing Protocols are
0:24
always constantly running and converging
0:27
and Recon converging so technically is
0:30
not an order to how you run these
0:32
protocols but for Simplicity let's
0:34
consider them one at a time so the first
0:37
one we'll consider is igp

## Slide 14: Combining Intra-Domain and Inter-Domain Routing
1. Use IGP to learn internal routes to others in the AS.
2. Use eBGP to learn external routes to other ASes.
B
D
A
G
AS#1
C
E
F
AS#5
AS#4
AS#3
AS#2
1. To reach G, my next-hop is F.
2. To reach Z, go via AS#5.
Z
Notes: to learn external
1:06
destinations we have to use bgp and bgp
1:10
we now know is a two-step process the
1:12
first step is to use ebgp for the Border
1:16
routers to discover external routes so
1:19
think of this as a B and G talking to
1:21
the outside world and learning external
1:24
routes for example G the Border router
1:28
might have learned that there is a path
1:29
to to Z via as number 5 so the Border
1:33
routers learn about some external routes
1:36
but remember that it's not enough for
1:38
the Border routers to know these routes
1:40
we need everyone in the as to know about
1:42
these routes

## Slide 15: Combining Intra-Domain and Inter-Domain Routing
1. Use IGP to learn internal routes to others in the AS.
2. Use eBGP to learn external routes to other ASes.
3. Use iBGP to distribute external routes to others in the AS.
B
D
A
G
AS#1
C
E
F
AS#5
AS#4
AS#3
AS#2
Z
3. To reach Z, exit via G.
1. To reach G, my next-hop is F.
2. To reach Z, go via AS#5.
Notes: so the
1:56
last step is to use ibgp to take those
1:59
EXT dnal routes that were learned by the
2:01
border routers and share them with the
2:03
whole class so for example G will tell
2:06
the whole class hey everyone I learned a
2:09
way to reach Z so if you ever want to
2:11
reach Z come talk to me and I will
2:13
forward the packet to Z for you that is
2:16
something that ibgp can announce and
2:19
notice that router e can now write that
2:21
information down router e writes down if
2:24
I ever want to talk to Z my buddy G
2:27
apparently knows how to reach Z so if I
2:30
ever want to talk to Z I will talk to my
2:32
buddy G and they will forward the packet
2:34
for me that is a route learned via
2:38
ibgp so in summary you use igp to learn
2:41
internal routes ebgp allows the Border
2:44
routers to learn the external routes and
2:47
then ibgp allows everyone to learn the
2:51
external routes because the Border
2:53
router announces it to the whole class
2:56
so that's what the picture looks like
2:57
when you put all the pieces together

## Slide 16: Combining Intra-Domain and Inter-Domain Routing
An egress router for a destination is a border router who can reach that destination.
Example: Inside AS#1, G is an egress router for Z.
G uses iBGP to tell local routers: "If you have packets for Z, send them to me."
B
D
A
G
AS#1
C
E
F
AS#5
AS#4
AS#3
AS#2
Z
3. To reach Z, exit via G.
1. To reach G, my next-hop is F.
2. To reach Z, go via AS#5.
Notes: this also introduces a term that you
3:04
haven't seen before called egress router
3:08
so an egress router is like the way to
3:10
exit the current as to reach an external
3:13
destination so if we look at the entry
3:16
that e wrote down as a result of ibgp e
3:20
wrote down if I ever want to talk to Z
3:23
the person I should talk to is G because
3:25
they can forward packets outside of the
3:28
current Network and closer to Z so in
3:31
other words G is the egress router for z
3:35
g is the way that you exit the current
3:37
Network to get closer to Z so the egress
3:41
routers are the Border routers you have
3:43
a choice between a B and G in this case
3:46
G is the egress router that you use to
3:49
exit the network and get closer to Z and
3:52
for example B would be the egress router
3:56
if I want to send packets to as number
3:58
two those packets would exit the current
4:00
network via B so everyone remembers the
4:04
egress routers for various destinations

## Slide 17: BGP and IGP Routing Tables
Every router now has two routing tables:
IGP table: Maps each internal destination to a next-hop.
BGP table: Maps each external destination to an egress router.
  The egress router is not necessarily a direct neighbor.
The two tables can be used to find the next hop for any destination.
Internal destinations: Just use the IGP table to find the next hop.
External destinations:
  First, use the BGP table to find the egress router.
  Then, use the IGP table to find the next-hop to the egress.
Notes: our routing tables will
0:13
actually now be two Separate Tables we
0:16
will have an igp table and that's the
0:19
one you've already seen from distance
0:21
vector or link state that Maps each
0:24
internal destination to a next toop it
0:27
says something like if you want to reach
0:29
internal destination H please send
0:31
packets to the next toop of e so it
0:34
tells me the direct next toop for
0:36
internal destinations the bgp table this
0:40
is the new one and the difference here
0:42
is we are now listing external
0:44
destinations ones outside of the network
0:47
and instead of listing a direct next
0:49
toop we instead list the egress router
0:52
we write down which exit do we take to
0:55
leave the current Network and get closer
0:57
to that external destination one thing
1:00
to note is that the egress router does
1:03
not need to be a direct neighbor and
1:05
that's actually okay

## Slide 18: BGP and IGP Routing Tables
B
D
A
G
AS#1
X
W
Y
C
E
F
AS#5
AS#4
AS#3
AS#2
Z
V
Internal Destinations | 
Destination | Next Hop
B | C
W | C
X | E
Y | E
G | E
... | ...
External Destinations | 
Destination | Egress via
U | A
V | B
Z | G
U
← D's two routing tables.
Notes: Is it obvious I ran out of letters.
so for example in
1:07
this picture notice that e writes down
1:11
that the exit to reach Z is G and G is
1:15
not a direct neighbor of e but that's
1:17
okay the egress router does not have to
1:20
be one of your direct neighbors you just
1:22
have to write down where you are exiting
1:24
the network to get closer to the Final
1:28
Destination so those are the two two
1:30
tables we are going to use and you can
1:32
combine using them to find destinations
1:35
and the next tops for any destination
1:38
that you want so if you want to find the
1:40
next toop for an internal destination
1:42
that's simple you just use the igp table
1:45
and look up the next top just like
1:47
you've been doing for distance vector or
1:49
link state for external destinations
1:52
it's a two-step process First Look up
1:55
the exit using the bgp table it tells
1:58
you what egress router to use to exit
2:01
the network and get closer to your
2:03
current destination and that erress
2:06
router might not be directly connected
2:08
to you and because that egress router
2:10
might not be directly connected to you
2:12
then use the igp table to find the next
2:15
top to get closer to the exit so the two
2:18
steps are where is the exit and what is
2:21
the next top to get closer to the exit

## Slide 19: BGP and IGP Routing Tables (in Router D)
To reach V, the egress router is B.
To reach B, the next hop is C.
Internal Destinations | 
Destination | Next Hop
B | C
W | C
X | E
Y | E
G | E
... | ...
External Destinations | 
Destination | Egress via
U | A
V | B
Z | G
B
D
A
G
AS#1
X
W
Y
C
E
F
AS#5
AS#4
AS#3
AS#2
Z
V
U
Notes: Is it obvious I ran out of letters.
let's say you are router D and
2:30
want to send packets somewhere well then
2:32
what you can do is use one of these two
2:34
tables and maybe both of them to find
2:38
the next top for any possible packet
2:40
that someone sends to you notice that
2:42
the internal destination table Maps
2:45
internal destinations b w x y g those
2:50
are all destinations inside of the
2:52
current Network and those are all mapped
2:54
to direct next Toops c e or a by
2:59
contrast the external destination table
3:02
is describing external destinations like
3:04
u v and z in other networks and there
3:08
instead of writing direct next Toops
3:10
we're writing the exit routers and some
3:13
of the exit routers like B and G are not
3:16
directly connected to us but that's okay
3:18
we're writing down the exit routers even
3:21
if they are far
3:22
away so how do you use these tables
3:25
let's say I want to send a packet to V
3:29
well the first thing I notice V is not
3:31
an internal destination it's an external
3:34
one so I go into my external destination
3:37
table and I look up the way to exit to
3:40
get closer to V it turns out that b is
3:44
the egress router that I should use to
3:46
exit the network and get closer to V so
3:50
in other words to get closer to V I must
3:52
exit via B that's what I learned from
3:55
the bgp table unfortunately B is not
3:59
directly connected to me so I can't just
4:01
forward this to B right away I need to
4:03
figure out how do I get this packet
4:05
closer to the exit closer to B to do
4:09
that I look in my internal destination
4:11
table and it says that the next hop to B
4:15
is C that's using the internal
4:18
destination table because B is an
4:20
internal destination so using the
4:23
internal destination table I realized
4:25
that the way to get closer to the exit
4:28
is to forward the table to C

## Slide 20: Implementing iBGP
Border routers use iBGP to distribute the routes it discovers to everyone else in the AS.
How is this actually implemented?
Many different approaches, though we'll assume a simple one.
B
D
A
G
AS#1
C
E
F
AS#5
AS#4
AS#3
AS#2
Z
Hey everyone, I just found a way to reach Z.
Notes: 0:02
one final note about ibgp and ebgp
0:05
before we move on is how ibgp is
0:09
actually implemented so far we've been
0:11
describing it very conceptually and
0:13
we've said if a border router like G
0:16
learns a way to reach Z what it should
0:19
do is just stand up and announce to
0:21
everyone else in the as that there is a
0:23
way to reach C and if you want to reach
0:25
G if you want to reach Z please exit via
0:30
G that's what we're doing so far when
0:32
you learn a route and you're a border
0:33
router stand up announce it to the whole
0:35
class how do you actually do that
0:38
there's lots of different approaches you
0:39
can look up something called route
0:41
reflectors if you want to find a more
0:43
sophisticated approach but let's use a
0:45
relatively simple one

## Slide 21: Implementing iBGP
The simple approach: Run an iBGP session between every pair of routers.
For N total routers and B border routers, requires ~ N × B sessions.
  Example: N = 7, B = 3 inside AS#1.
Could be a scaling issue on larger networks.
AS#1
AS#5
AS#4
AS#3
AS#2
Z
B
D
A
G
F
Hey everyone, I just found a way to reach Z.
Note: iBGP sessions are still forwarding packets across multiple hops (we aren't building new links).
E
C
Notes: so our approach is
0:48
going to be to run an ibgp session
0:51
between every pair of routers remember
0:55
that an ibgp session is two routers
0:58
constantly communicating data between
1:00
each other so for example we can start a
1:02
session between G and a and another
1:05
session between G and B and another one
1:07
between G and C G and D G and E GN F and
1:12
when you want to announce something to
1:14
the class you send a packet to a you
1:16
send one to B you send one to C another
1:18
one to D another one to e and another
1:21
one to F so G is going to send six
1:24
separate packets in order to announce
1:27
this new information to the six
1:29
different routers in the as this works
1:32
it doesn't scale terribly well because
1:35
it requires having a lot of bgp sessions
1:38
in fact you need one between every
1:39
border router and everyone else so a
1:42
would need sessions with everyone else
1:44
and B would also need sessions for
1:47
everyone else on a larger Network this
1:49
could present scaling issues but that's
1:51
the simple approach that we will use and
1:54
remember that when you create an ibgp
1:57
session you were not building a new link
2:00
between G and a you are just saying that
2:02
G and a are going to exchange data and
2:04
the data that they exchange still has to
2:07
travel multiple hops so for example the
2:10
G to a packet would travel g f e d a and
2:15
then G sends a separate packet to B
2:17
which travels the path g f e c b and so
2:21
on and so forth so there's no new links

## Slide 22: Multiple Links Between ASes
BGP Implementation
External BGP and Internal BGP
Multiple Links Between ASes
Message Types and Route Attributes
Issues with BGP
IP Header
IPv4 Header Fields
IPv6 Changes
Security
Lecture 9, Spring 2026
Notes: 0:02
let's talk about installing multiple
0:04
links between a pair of as's and how
0:07
this changes some of the assumptions
0:09
that we've seen so far

## Slide 23: Multiple Links Between ASes
With only a single link between AT&T and Verizon, packets might travel long routes.
A
B
C
F
G
H
D
I
E
J
Verizon
AT&T
Notes: https://commons.wikimedia.org/wiki/File:PNGedUSoutline.png
consider these two as's Verizon
0:32
and AT&T they are very big as's they
0:35
span the entire country and let's say
0:38
there's only one link between them and
0:40
that link is on the west coast of the
0:42
United States between a and F so because
0:46
there's only one link between these as's
0:48
and it's on the west coast this means
0:50
that if e wants to send a message to J
0:54
the way that it would do so is actually
0:56
to send the packet all the way across
0:58
the country to a and then a will forward
1:01
it to F in AT&T's network and then f is
1:04
going to have to forward the packet all
1:06
the way back across the country to J
1:09
this is quite wasteful this packet is
1:11
taking an unnecessarily long route and
1:13
it wastes the resources of Verizon and
1:16
AT&T because they have to carry this
1:19
packet all the way across the country
1:21
and then all the way
1:23
back

## Slide 24: Multiple Links Between ASes
Adding a second link between AT&T and Verizon creates shorter routes.
A
B
C
F
G
H
D
I
E
J
Verizon
AT&T
Notes: https://commons.wikimedia.org/wiki/File:PNGedUSoutline.png
a better approach would be to
1:26
actually have two links between this
1:28
pair of as's so there's one link on the
1:31
west coast and one link on the east
1:33
coast and now if e and J want to talk to
1:36
each other we no longer have to send the
1:38
packet all the way across the country
1:40
and back so this is a better approach
1:43
but do notice that we are now
1:44
introducing something we haven't seen
1:46
before these are two as's and we've
1:49
drawn two parallel lines between them so
1:52
unlike all the pictures so far where any
1:55
pair of as's are connected by just a
1:58
single line there could now be a case
2:00
where I draw two parallel lines between
2:03
as number 3 and as number four and
2:06
that's going to introduce some
2:07
tiebreaking scenarios that we haven't
2:09
seen before namely which of those two
2:12
links do you use they look the same
2:14
they're two lines between the same pair
2:16
of as's

## Slide 25: Multiple Links Between ASes
Verizon
There can be multiple paths between the same two ASes.
From the AS graph perspective, both routes are identical.
If you're AT&T, which route do you prefer?
Gao-Rexford rules won't help – the next AS is Verizon in both routes.
A
B
E
F
G
C
H
D
I
AT&T
X
Y
Notes: https://commons.wikimedia.org/wiki/File:PNGedUSoutline.png
the existence of multiple links
2:36
between as's creates some tiebreaking
2:38
scenarios that we haven't seen before if
2:41
you think about the conceptual picture
2:43
of bgp from last time we were always
2:46
thinking at the as level we were drawing
2:49
out paths between as's and we would draw
2:51
a path that says something like as
2:53
number three to as number 10 to Asos
2:56
number 25 you'd write out the path as a
2:59
list of as's the problem is if you have
3:03
two parallel links between two as's well
3:06
then the path that you create looks the
3:10
same if you're thinking at the as level
3:13
so for example if there's two parallel
3:15
links between A&T and Verizon which link
3:18
you use is indifferent at the as level
3:21
they create the same as path so for
o if Verizon is a
3:49
customer both of these links point at a
3:51
customer if Verizon is a peer both of
3:54
these links point at appear because they
3:56
are pointing at the same as so you can't
3:59
use the xer rules to pick the customer
4:01
over the pier since the links are
4:03
between the same pair of as's it's going
4:06
to say customer customer or peer peer or
4:10
provider provider you can't use the gxf
4:13
rules to help you tiebreak so we need
4:15
additional tie Breakers to help us

## Slide 26: Hot Potato Routing
All else equal, an AS prefers the route that uses the least of its own resources.
AT&T prefers the gold path, where the packet mostly travels on Verizon's AS.
Hot potato routing: Get rid of the packet ASAP, and make someone else carry it the rest of the way.
As AS prefers the nearest egress router (if there are multiple).
Verizon
A
B
E
F
G
C
H
D
I
AT&T
X
Y
Notes: https://commons.wikimedia.org/wiki/File:PNGedUSoutline.png
the first tiebreak we'll see is
0:02
something called Hot Potato routing so
0:04
in this example let's say x wants to
0:07
send packets to Y and it turns out there
0:10
are two paths that the packet can take
0:13
from the as perspective they look
0:15
identical they go from AT&T to Verizon
0:18
so we need to use a tiebreaking scheme
0:21
to decide which path we like better so
0:24
if you AT&T let's say you're router e
0:27
inside of AT&T's network and you need to
0:30
forward this packet how should you do it
0:33
do you want to forward the packet along
0:34
the Gold Path or the pink one well let's
0:38
think in terms of AT&T AT&T is a
0:41
business it likes making money and it
0:43
doesn't like wasting money when it
0:45
doesn't have to if we allow this packet
0:48
to take the path in Gold we are dumping
0:50
this packet off to Verizon and forcing
0:53
Verizon to carry the packet most of the
0:55
way so if you imagine these networks as
0:58
spanning the entire country then what
1:00
would happen in the Gold Path is we give
1:03
the packet to Verizon in San Francisco
1:05
and we force Verizon to carry the packet
1:08
all the way across the country to New
1:10
York by contrast in the pink path AT&T
1:14
is doing most of the work AT&T is using
1:17
its own resources and paying to carry
1:20
the packet all the way across the
1:22
country to New York and only dumping the
1:25
packet off to Verizon once it reaches
1:27
New York so if you're AT&T you prefer
1:30
the Gold Path because it's cheaper for
1:32
you

## Slide 27: Hot Potato Routing
All else equal, an AS prefers the route that uses the least of its own resources.
AT&T prefers the gold path, where the packet mostly travels on Verizon's AS.
Hot potato routing: Get rid of the packet ASAP, and make someone else carry it the rest of the way.
As AS prefers the nearest egress router (if there are multiple).
Verizon
A
B
E
F
G
C
H
D
I
AT&T
X
Y
[eBGP] I can reach Y.
[eBGP] I can reach Y.
Notes: https://commons.wikimedia.org/wiki/File:PNGedUSoutline.png
the way that you
2:15
actually Implement Hot Potato routing is
2:18
you find the nearest exit if there are
2:20
multiple exits to the same as so in this
2:23
case f and I are both exits to Verizon
2:27
so if we're router e we prefer for the
2:30
closer one because that allows us to get
2:32
rid of the packet and make someone else
2:34
namely Verizon do all of the work so it
2:38
might look something like this first we
2:40
use ebgp to learn about the routes to
2:43
Verizon A and D both announce that they
2:46
can reach Y and that information
2:49
propagates to AT&T so F and I both know
2:54
that they can now reach y but it's not
2:56
enough for f and I to know they also
2:59
have to announce their findings to the
3:00
rest of the class using
3:02
ibgp so F and I both use ibgp to
3:06
announce to everyone hey everyone inside
3:08
of AT&T I have a path to Y so if you
3:11
want to forward packets to Y you can
3:14
send them to me f and I'll dump them off
3:16
for you or you can send the packets to
3:19
me I and router I will forward the
3:22
packets to Y for you so both of them
3:25
announc that they can reach y and e is
3:27
now aware of both exits e knows that f
3:30
is a valid exit to Y and I is also a
3:34
valid exit to
3:36
Y so now when e receives a packet
3:40
destined for y it can choose either f or
3:43
i as a valid exit

## Slide 28: Hot Potato Routing
Verizon
A
B
E
F
G
C
H
D
I
AT&T
X
Y
All else equal, an AS prefers the route that uses the least of its own resources.
AT&T prefers the gold path, where the packet mostly travels on Verizon's AS.
Hot potato routing: Get rid of the packet ASAP, and make someone else carry it the rest of the way.
As AS prefers the nearest egress router (if there are multiple).
[iBGP] Hi everyone, I have a path to Y.
[iBGP] Hi everyone, I have a path to Y.
Notes: https://commons.wikimedia.org/wiki/File:PNGedUSoutline.png

## Slide 29: Hot Potato Routing
All else equal, an AS prefers the route that uses the least of its own resources.
AT&T prefers the gold path, where the packet mostly travels on Verizon's AS.
Hot potato routing: Get rid of the packet ASAP, and make someone else carry it the rest of the way.
As AS prefers the nearest egress router (if there are multiple).
Verizon
A
B
E
F
G
C
H
D
I
AT&T
X
Y
I and F can both reach Y using the same AS path.
I'll use F to exit since it's closer.
Notes: https://commons.wikimedia.org/wiki/File:PNGedUSoutline.png

## Slide 30: Multiple Links Between ASes
Verizon
What if two egress routers are equally close?
AT&T is indifferent between the paths.
If you're Verizon, which route do you prefer?
B
C
F
G
H
D
I
E
J
AT&T
X
Y
A
Notes: https://commons.wikimedia.org/wiki/File:PNGedUSoutline.png
from AT&T's perspective
1:03
both of these routes are equally good
1:06
now let's think about Verizon if you're
1:08
Verizon do you have a preference of
1:11
which path it takes the gold one or the
1:13
pink one well you sure do if you're a
1:16
Verizon you have the same business
1:18
incentive of not using resources to
1:20
carry this packet so if you're a Verizon
1:23
you don't like this Gold Path because it
1:26
requires you to send the packet all the
1:27
way across the country you really prefer
1:30
the pink path so what we can do to
1:33
resolve this type breaker because AT&T
1:36
has no preference we're going to ask
1:39
Verizon for its opinions and let
1:41
Verizon's preferences take over so when
1:44
AT&T doesn't have its own preference
1:47
we're going to ask Verizon what its
1:49
preference is and follow what Verizon
1:51
says in order to encode Verizon's
1:55
preference that it prefers the pink path
1:57
over the Gold Path Verizon
2:00
advertisements will now contain an extra
2:03
value

## Slide 31: Multi-Exit Discriminator (MED)
Verizon
All else equal, an AS prefers the route that uses the least of its own resources.
Verizon prefers the pink path, because E is closer to the destination than A.
Using the closer border router = Verizon uses less bandwidth.
When announcing routes, include a Multi-Exit Discriminator (MED).
MED represents distance from router to destination. Lower number is preferred.
B
C
F
G
H
D
I
E
J
AT&T
X
Y
A
Notes: https://commons.wikimedia.org/wiki/File:PNGedUSoutline.png

## Slide 32: Multi-Exit Discriminator (MED)
Verizon
All else equal, an AS prefers the route that uses the least of its own resources.
Verizon prefers the pink path, because E is closer to the destination than A.
Using the closer border router = Verizon uses less bandwidth.
When announcing routes, include a Multi-Exit Discriminator (MED).
MED represents distance from router to destination. Lower number is preferred.
B
C
F
G
H
D
I
E
J
AT&T
X
Y
A
[eBGP] I can reach Y. It's 5 away from me.
[eBGP] I can reach Y. It's 1 away from me.
Notes: https://commons.wikimedia.org/wiki/File:PNGedUSoutline.png

## Slide 33: Multi-Exit Discriminator (MED)
Verizon
All else equal, an AS prefers the route that uses the least of its own resources.
Verizon prefers the pink path, because E is closer to the destination than A.
Using the closer border router = Verizon uses less bandwidth.
When announcing routes, include a Multi-Exit Discriminator (MED).
MED represents distance from router to destination. Lower number is preferred.
B
C
F
G
H
D
I
E
J
AT&T
X
Y
A
[iBGP] Hi everyone, I have a path to Y.
The other AS said this path has MED=5.
[iBGP] Hi everyone, I have a path to Y.
The other AS said this path has MED=1.
Notes: https://commons.wikimedia.org/wiki/File:PNGedUSoutline.png

## Slide 34: Multi-Exit Discriminator (MED)
Verizon
All else equal, an AS prefers the route that uses the least of its own resources.
Verizon prefers the pink path, because E is closer to the destination than A.
Using the closer border router = Verizon uses less bandwidth.
When announcing routes, include a Multi-Exit Discriminator (MED).
MED represents distance from router to destination. Lower number is preferred.
B
C
F
G
H
D
I
E
J
AT&T
X
Y
A
F and J are equally far away.
I'll use J, since it's got a lower MED.
Notes: https://commons.wikimedia.org/wiki/File:PNGedUSoutline.png

## Slide 35: Importing and Exporting with Tiebreaking Policies
Exporting rules:
Use Gao-Rexford rules to decide which ASes hear about this route.
In the announcement, include the MED (distance from router to destination). Lower MED = Prefer to use this router.
Importing rules, in order of priority:
Use Gao-Rexford rules (customer > peer > provider).
  Goal: Save money.
If 1 tied: Pick the shorter path (the path passing through fewer ASes).
  Goal: Maximize performance.
If 1-2 tied: Pick the path with the nearest egress router (hot potato routing).
  Goal: Minimize use of my network bandwidth.
If 1-3 tied: Pick the path with the lower MED.
If 1-4 tied: Arbitrary tiebreaker (e.g. pick router with lower IP address).

## Slide 36: Hot Potato Routing and MED are Contradictory
The importing and exporting ASes both want to minimize their own link usage.
Importing AS (AT&T) does this with hot potato routing: Pick the nearest egress.
Exporting AS (Verizon) does this with MED: Send me the packet on the closest router.
Verizon
A
B
E
F
G
C
H
D
I
AT&T
X
Y
AT&T prefers gold path.
Verizon prefers pink path.

## Slide 37: Hot Potato Routing and MED are Contradictory
The importing and exporting ASes both want to minimize their own link usage.
Importing AS (AT&T) does this with hot potato routing: Pick the nearest egress.
Exporting AS (Verizon) does this with MED: Send me the packet on the closest router.
Verizon
A
B
E
F
G
C
H
D
I
AT&T
X
Y
MED = 5 Don't send it this way.
Closer egress router
Send it this way please.
AT&T prefers gold path.
Verizon prefers pink path.

## Slide 38: Hot Potato Routing and MED are Contradictory
The importing and exporting ASes both want to minimize their own link usage.
Importing AS (AT&T) does this with hot potato routing: Pick the nearest egress.
Exporting AS (Verizon) does this with MED: Send me the packet on the closest router.
Verizon
A
B
E
F
G
C
H
D
I
AT&T
X
Y
MED = 1
Send it this way please.
Further egress router Don't send it this way.
AT&T prefers gold path.
Verizon prefers pink path.

## Slide 39: Hot Potato Routing and MED are Contradictory
Hot potato routing can lead to asymmetric paths.
X → Y traffic: AT&T ditches packet quickly, Verizon carries it most of the way.
Y → X traffic: Verizon ditches packet quickly, AT&T carries it most of the way.
Verizon
A
B
E
F
G
C
H
D
I
AT&T
X
Y

## Slide 40: Message Types, Route Attributes
BGP Implementation
External BGP and Internal BGP
Multiple Links Between ASes
Message Types and Route Attributes
Issues with BGP
IP Header
IPv4 Header Fields
IPv6 Changes
Security
Lecture 9, Spring 2026
Notes: 0:01
we now have all the pieces we need to
0:03
implement bgp with multiple routers
0:07
inside of an as working together as one
0:09
cohesive brain but everything we've done
0:12
so far is in English and using speech
0:15
bubbles so for example we had pictures
0:19
like this or we said send it this way
0:21
further eress router but of course real
0:23
life routers cannot use speech bubbles
0:25
to communicate and they cannot write
0:27
plain English so the final thing we need
0:30
to do is Implement all of our policies
0:33
in actual code

## Slide 41: Implementing BGP: Message Types
To implement BGP, we need to specify:
Syntax: Format of BGP message.
Semantics: How to process BGP messages.
There are 4 BGP message types:
Open: Start a BGP session.
KeepAlive: I'm still here, don't close the BGP session.
Notification: An error occurred.
Update: Announce a route.
  Could be a new route, an update to an old route, or withdrawing a route.
  We'll focus on this one.
Notes: so to do that we're going to
0:41
need to specify the syntax and the
0:44
semantics of pgp remember that protocols
0:47
require syntax and semantics the syntax
0:50
tells us what the ones and zeros
0:52
represents and the semantics tell us
0:54
what to do when we receive a message so
0:57
now we're going to focus on how to
0:59
actually write bgp syntax how do you
1:01
write these messages that we've been
1:03
writing in plain English in actual ones
1:05
and zeros to do so we need to Define bgp
1:09
message types these are the messages
1:11
that the routers exchange during bgp
1:15
there are four types we'll just focus on
1:17
one but do know that other message types
1:19
exist there's the open message for
1:21
starting bgp sessions the keep aive
1:24
message for maintaining a bgp session
1:27
it's like when you're talking on the
1:28
phone and neither person is talking you
1:30
might occasionally want to say hey I'm
1:32
still here don't hang up yet we might
1:34
have more to say there's also the
1:37
somewhat strangely named notification
1:40
message for errors I don't know why they
1:42
called it that but as far as I can tell
1:44
that is for processing errors but we're
1:46
going to focus on the update message
1:49
because the update message is how you
1:51
encode the announcements so all of those
1:53
announcements that we've been seeing
1:55
ebgp ibgp sharing with the class all of
1:59
those are bgp announcements and they're
2:01
going to be encoded in bgp update
2:05
messages so that's what we're going to
2:07
look
2:08
at

## Slide 42: BGP Update Message Format
Update message encodes an announcement using two values:
Destination prefix.
One or more route attributes.
Route attributes:
Used to express properties about routes.
Can be used in route import/export decisions.
Written as name-value pairs.
Some attributes are local: Only announced in iBGP.
Some attributes are global: Announced in eBGP.
There are many standardized attributes, but we'll look at 3.
Notes: so bgp update messages how do you
2:12
actually encode them every bgp update
2:15
message will first have a destination
2:18
prefix indicating what destination we're
2:20
talking about so every advertisement has
2:23
to say something like I can reach Z or I
2:26
can reach V or I can reach w
2:30
that is the destination prefix that we
2:32
have to include but of course instead of
2:34
saying Z or w we actually use IP
2:38
prefixes so the destination prefix might
2:40
be something like 1 19211
2:45
12.0.0 sl16 it's a range of IP addresses
2:49
like we've already seen and that
2:52
indicates what destination you are
2:54
announcing that you can reach in
2:56
addition to the destination prefix we
2:59
will also include include one or more
3:00
route attributes and this incudes the
3:03
additional information that we've been
3:05
talking about things like the path that
3:08
the packet will take or the me value
3:11
those are going to be encoded in the
3:13
route attributes you can think of these
3:15
like name value pairs like a python
3:18
dictionary where the name tells us what
3:20
the attribute is and the value tells us
3:22
the actual value of the attribute in
3:25
this particular advertisement

## Slide 43: Route Attribute #1: ASPATH
Name: ASPATH. Value: List of all ASes in this route, in reverse order.
Scope: Global (included in both eBGP and iBGP announcements).
AS#25
128.112.0.0/16
AS#72
AS#3
AS#91
eBGP Announcement:
Destination = 128.112.0.0/16
ASPATH = [3, 72, 25]

## Slide 44: Route Attribute #2: LOCAL PREFERENCE
AS#91
Name: LOCAL PREFERENCE. higher is more preferred.
Scope: Local (only included in iBGP announcements).
Used to encode policy preference between AS paths (e.g. Gao-Rexford rules).
C
AS#79
(Peer)
iBGP Announcement:
Destination = 128.112.0.0/16
ASPATH = [79, 25]
LOCAL PREF = 1000
D
E
A
B
AS#7
(Customer)
AS#25
128.112.0.0/16
iBGP Announcement:
Destination = 128.112.0.0/16
ASPATH = [7, 25]
LOCAL PREF = 3000
100 and 300 would have worked, too. Only the relative ranking matters.

## Slide 45: Route Attribute #3: MED
Name: MED. lower is more preferred. Scope: Global (included in both eBGP and iBGP announcements). Used when there are multiple links between ASes. Specifies distance from announcing router to destination.
B
C
F
G
H
D
I
E
J
AS#19
A
AS#72
AS#25
128.112.0.0/16
eBGP Announcement:
Destination = 128.112.0.0/16
ASPATH = [72, 25]
MED = 4
eBGP Announcement:
Destination = 128.112.0.0/16
ASPATH = [72, 25]
MED = 1

## Slide 46: Import Policy with Attributes
Priority | Rule | Implementation | Goal
1 | Gao-Rexford rules | Highest LOCAL PREF | Make/save money
2 | Shortest path | Shortest ASPATH length | Maximize performance
3 | Hot potato routing | Nearest egress router (lowest IGP cost) | Minimize use of my bandwidth
4 | Multiple links: Send to router closer to destination | Smallest MED | Minimize use of other AS's bandwidth
5 | Arbitrary | Lowest router IP | N/A

## Slide 47: Issues with BGP
BGP Implementation
External BGP and Internal BGP
Multiple Links Between ASes
Message Types and Route Attributes
Issues with BGP
IP Header
IPv4 Header Fields
IPv6 Changes
Security
Lecture 9, Spring 2026

## Slide 48: Issues with BGP
Security:
No guarantee that an AS owns the prefixes it advertises.
No guarantee that an AS will follow the path it advertises.
Performance trade-offs:
Policy-based paths are not always least-cost.
AS path length can be misleading (path inside an AS could be 1 hop or 100 hops).
Complicated and prone to misconfiguration:
Many BGP attributes. Configuration is often manual and ad-hoc.
BGP misconfiguration is a major source of Internet outages!
Invalid routes:
Reachability and convergence are not guaranteed without Gao-Rexford.
Notes: 0:01
to wrap up bgp let's talk about some
0:03
issues with it so it turns out bgp is a
0:07
remarkably good protocol it has stood
0:09
the test of time it's been around for 20
0:11
30 years and everyone on the internet
0:13
uses it so it's pretty impressive that
0:15
the entire internet uses bgp and is
0:18
still working I find that a very
0:20
impressive achievement that being said
0:22
there are still some issues that we
0:23
should talk about one issue is security
0:26
there is no built-in security measures
0:29
into BG P so it means that as's are
0:32
allowed to lie and specifically some
0:35
things it might lie about maybe it lies
0:37
about being able to reach a destination
0:39
that it actually cannot so the as says I
0:42
can reach destination Z but it actually
0:45
can't that could be a security issue and
0:48
another security issue might be that the
0:50
as says it's going to follow One path
0:52
but ends up following a different one so
0:54
it advertises an as path and it says I'm
0:57
forwarding this packet from 9 to 7 to 12
1:01
but when it receives the packet it
1:03
actually forwards it along a different
1:05
path of as's so as's are allowed to lie
1:09
the protocol by itself doesn't stop that
1:11
and there is some ongoing research about
1:13
ways to actually build security into
1:16
this protocol but the base protocol does
1:19
not stop Asis from lying another issue
1:23
is performance and this is one that's
1:26
not really an issue in that it's not a
1:28
problem but it's a conscious tradeoff
1:31
that the designers of bgp made so
1:34
because bgp values the autonomy and the
1:38
privacy of each as it means that the
1:41
paths that are chosen are often not
1:44
least cost we're respecting everyone's
1:46
policies of making money or whatever
1:49
other weird policy they have and as a
1:51
result we are not strictly optimizing
1:54
for cost you can imagine a different bgp
1:56
design where we ignore everyone's
1:59
autonomy and we go for the least cost
2:01
paths but that is not what the bgp
2:03
designers did they chose to
2:05
intentionally sacrifice a little bit of
2:08
performance in exchange for allowing
2:11
everyone to have their own special
2:14
policy also because of the privacy and
2:17
autonomy concerns we list the as paths
2:20
in terms of the as's that the packet
2:23
passes through so the advertisement says
2:25
I can reach Z via as 7 12 and 13
2:30
but we have no idea how big those as's
2:32
are there could be one hop inside that
2:34
as that as could be carrying the packet
2:37
across hundreds of hops from our
2:39
perspective this is length three either
2:41
way because it passes through three as's
2:44
regardless of their length so the as
2:47
path length can be misleading this is
2:49
another case where we did a tradeoff and
2:51
the designer said it's okay if the paths
2:53
are a little bit too long or longer than
2:57
optimal but at least we're respecting
2:59
everyone's privacy and not forcing Asis
3:02
to reveal their internal structure so
3:05
while you could call this an issue I
3:07
think it's more of a trade-off where
3:09
they intentionally sacrific performance
3:11
in exchange for autonomy and
3:14
privacy another issue with bgp it is
3:17
quite complicated we're just showing you
3:19
the basics there's a lot of edge cases
3:21
that we haven't talked about and also a
3:24
lot of bgp has to be manually configured
3:27
for example when we talked about local
3:29
PR
3:30
where you indicate the gal rexord Rules
3:32
by saying that customers are 3,000 and
3:35
peers are 1,000 someone has to go in and
3:38
manually type those numbers and if they
3:41
make a mistake well suddenly the policy
3:43
might not be what you expect and often
3:46
times Internet outages are caused by
3:49
manual operators messing up bgp there is
3:52
some research into automatically
3:55
configuring bgp but the base protocol
3:57
requires a manual configuration and that
4:00
is prone to human errors and the final
4:03
issue with bgp is that it does not come
4:05
with any guarantees we did have a proof
4:08
that said if everyone follows the G
4:10
Rexford rules we are going to be able to
4:14
reach every destination and the routes
4:16
will converge but that proof assumed
4:19
everyone was following the gal Rexford
4:21
rules if someone is not following those
4:24
rules we can't use that proof and all
4:26
bets are off is it actually possible to
4:28
reach all internet destinations we no
4:31
longer have that guarantee so that's
4:34
another issue with bgp but despite these
4:37
issues I still think it's a very
4:39
impressive protocol given that the
4:41
entire internet uses it and it's one of
4:43
the backbone protocols for making
4:45
everything work so that's actually it
4:47
for bgp hope you enjoyed all of the
4:50
intricacies of the protocol I think it's
4:52
a pretty fun protocol that talks about
4:54
real life business goals in addition to
4:57
you know leas cost routing and other
4:59
things we've seen

## Slide 49: IPv4 Header Fields
BGP Implementation
External BGP and Internal BGP
Multiple Links Between ASes
Message Types and Route Attributes
Issues with BGP
IP Header
IPv4 Header Fields
IPv6 Changes
Security
Lecture 9, Spring 2026
Notes: 0:01
in the second half of today we'll
0:03
conclude our discussion of layer three
0:06
protocols by talking about all of the
0:08
different fields in the IP headers we'll
0:11
start with ipv4 then we'll talk about
0:14
IPv6 and then we'll be
0:16
done

## Slide 50: IP Header Design Goals
Think of the IP header as an interface.
Allows the source and intermediate routers to exchange information.
Allows the source and destination to exchange information.
Design goals:
Small. A larger IP header makes every single packet larger.
Simple. Routers have to process packets quickly.
What fields are in the IP header?
It depends on what tasks IP needs to perform.
Version (4) | Hdr len (4) | Type of Service (8) |  | Total Length in Bytes (16) |  |  | 
Identification (16) |  |  |  | Flags (3) | Fragment Offset (13) |  | 
TTL (8) |  | Protocol (8) |  | Header Checksum (16) |  |  | 
Source IP Address (32) |  |  |  |  |  |  | 
Destination IP Address (32) |  |  |  |  |  |  | 
Options (if any) |  |  |  |  |  |  | 
Payload |  |  |  |  |  |  | 
Notes: 1:01Our goal:
Understand all of the fields in this header.
Understand the design choices in making this header.
so if we're getting into the heads of
1:03
the IP designers and we're thinking like
1:05
a designer we can think of the IP header
1:08
as the way that routers and hosts
1:11
communicate at layer 3 so if we're
1:14
forwarding a packet across the network
1:16
and the end host has to say something to
1:18
the router it would do so by filling in
1:20
the IP header with some data or if one
1:23
router wants to say something to the
1:25
later routers it would do so by filling
1:27
in an IP field and then forwarding the p
1:29
packet so if routers or hosts want to
1:32
communicate they have to use the fields
1:35
in the IP header to talk to each other
1:38
so therefore one way to design the IP
1:40
header is to think about what things the
1:43
routers and the hosts might want to say
1:46
to each other what do they want to talk
1:48
about what functionality do they have
1:51
that they need to express in the header
1:53
that can give us a clue as to what
1:55
Fields have to be in the headers and
1:57
what Fields don't so we're going to
1:58
split up the header into various tasks
2:01
that have to happen at layer three and
2:03
for each task we'll see what headers are
2:06
relevant for that task by breaking down
2:09
the problem like this it allows us to
2:11
think about what fields are there and
2:13
also why they were added

## Slide 51: IP Tasks
IP functionality can be classified into 6 tasks.
Some tasks are done by only routers or the destination host. Others are done by both.
Parse the packet. (both router and destination)
Forward packet to the next hop. (router only)
Tell the destination what to do next. (destination only)
Send responses back to the source. (both router and destination)
Handle errors. (both router and destination)
Specify any special packet handling. (both router and destination)

## Slide 52: Task #1: Parse the Packet
Version: What version of IP?
Header length (measured in 4-byte words): Where does the header end?
Total length (measured in bytes): Where does the packet end?
Version (4) | Hdr len (4) | Type of Service (8) |  | Total Length in Bytes (16) |  |  | 
Identification (16) |  |  |  | Flags (3) | Fragment Offset (13) |  | 
TTL (8) |  | Protocol (8) |  | Header Checksum (16) |  |  | 
Source IP Address (32) |  |  |  |  |  |  | 
Destination IP Address (32) |  |  |  |  |  |  | 
Options (if any) |  |  |  |  |  |  | 
Payload |  |  |  |  |  |  | 

## Slide 53: Task #2: Forward Packet to Next Hop
Destination IP address.
Version (4) | Hdr len (4) | Type of Service (8) |  | Total Length in Bytes (16) |  |  | 
Identification (16) |  |  |  | Flags (3) | Fragment Offset (13) |  | 
TTL (8) |  | Protocol (8) |  | Header Checksum (16) |  |  | 
Source IP Address (32) |  |  |  |  |  |  | 
Destination IP Address (32) |  |  |  |  |  |  | 
Options (if any) |  |  |  |  |  |  | 
Payload |  |  |  |  |  |  | 

## Slide 54: Task #3: Tell Destination What to Do Next
Protocol field: Identify the Layer 4 protocol to pass the payload to.
Version (4) | Hdr len (4) | Type of Service (8) |  | Total Length in Bytes (16) |  |  | 
Identification (16) |  |  |  | Flags (3) | Fragment Offset (13) |  | 
TTL (8) |  | Protocol (8) |  | Header Checksum (16) |  |  | 
Source IP Address (32) |  |  |  |  |  |  | 
Destination IP Address (32) |  |  |  |  |  |  | 
Options (if any) |  |  |  |  |  |  | 
Payload |  |  |  |  |  |  | 

## Slide 55: Task #3: Tell Destination What to Do Next
We need to indicate which protocol should handle the packet next.
De-multiplexing: Picking one of several possible L4 protocols.
IP Header
IP Payload
Without the protocol field, we have no idea what to do with the payload.
IP Header
Protocol = 6
TCP Payload
If we see protocol = 6:
Pass the payload to TCP code.
IP Header
Protocol = 17
UDP Payload
TCP Header
UDP Header
If we see protocol = 17:
Pass the payload to UDP code.

## Slide 56: Task #4: Send Responses Back to Source
Source IP address.
Note: We said both the router and destination might do this.
The router might want to send a response back to the source too (e.g. if an error occurs).
Version (4) | Hdr len (4) | Type of Service (8) |  | Total Length in Bytes (16) |  |  | 
Identification (16) |  |  |  | Flags (3) | Fragment Offset (13) |  | 
TTL (8) |  | Protocol (8) |  | Header Checksum (16) |  |  | 
Source IP Address (32) |  |  |  |  |  |  | 
Destination IP Address (32) |  |  |  |  |  |  | 
Options (if any) |  |  |  |  |  |  | 
Payload |  |  |  |  |  |  | 

## Slide 57: Task #5: Handle Errors: TTL
Problem: Forwarding loops cause packets to cycle indefinitely. Wastes bandwidth.
Time-to-live (TTL): Specifies maximum number of hops a packet can take.
TTL is decremented at every hop by the router.
If router receives packet with TTL 1:
  Discard packet.
  Send a "time exceeded" message back to the source.
Version (4) | Hdr len (4) | Type of Service (8) |  | Total Length in Bytes (16) |  |  | 
Identification (16) |  |  |  | Flags (3) | Fragment Offset (13) |  | 
TTL (8) |  | Protocol (8) |  | Header Checksum (16) |  |  | 
Source IP Address (32) |  |  |  |  |  |  | 
Destination IP Address (32) |  |  |  |  |  |  | 
Options (if any) |  |  |  |  |  |  | 
Payload |  |  |  |  |  |  | 

## Slide 58: Task #5: Handle Errors: Checksum
Problem: The packet could get corrupted in transit.
Checksum: Small number of bits used to verify that data hasn't been corrupted.
If checksum is incorrect, router/destination discards packet.
Version (4) | Hdr len (4) | Type of Service (8) |  | Total Length in Bytes (16) |  |  | 
Identification (16) |  |  |  | Flags (3) | Fragment Offset (13) |  | 
TTL (8) |  | Protocol (8) |  | Header Checksum (16) |  |  | 
Source IP Address (32) |  |  |  |  |  |  | 
Destination IP Address (32) |  |  |  |  |  |  | 
Options (if any) |  |  |  |  |  |  | 
Payload |  |  |  |  |  |  | 

## Slide 59: Task #5: Handle Errors: Checksum
The checksum is only computed on the IP header, not the payload.
IP header can't detect the payload being corrupted
Why this design? End-to-end principle. The payload should be checked by the end hosts, not intermediate routers.
The checksum has to be updated at every router.
Why? Because the TTL changes.
Alternate design: Don't include the TTL in the checksum. Now, routers don't have to recompute checksum (less work for routers).

## Slide 60: Task #5: Handle Errors: Fragmentation
Problem: The packet might be too large for a link.
Every link has a Maximum Transmission Unit (MTU): Largest number of bits the link can carry as one unit.
If a packet size exceeds a link's MTU, the router must split the packet into multiple fragments.
Then, the host has to reassemble the fragments to recover the original packet.

## Slide 61: Task #5: Handle Errors: Fragmentation
Problem: The packet might be too large for a link.
ID: Each fragment of the same packet has the same ID.
Flags (3 bits, 1 bit unused):
DF: Don't Fragment. If this packet is too large, just drop it.
MF: More Fragments. There's more data after this fragment.
Offset: Identifies which bytes of the original packet are in this fragment.
Version (4) | Hdr len (4) | Type of Service (8) |  | Total Length in Bytes (16) |  |  | 
Identification (16) |  |  |  | Flags (3) | Fragment Offset (13) |  | 
TTL (8) |  | Protocol (8) |  | Header Checksum (16) |  |  | 
Source IP Address (32) |  |  |  |  |  |  | 
Destination IP Address (32) |  |  |  |  |  |  | 
Options (if any) |  |  |  |  |  |  | 
Payload |  |  |  |  |  |  | 

## Slide 62: Task #5: Handle Errors: Fragmentation
IP Header
ID:
DF = F, MF = F
Offset:
IP Header
ID: 25930
DF = F, MF = T
Offset: 0
IP Payload
(Bytes 0~1000)
IP Payload
(Bytes 1000~2000)
IP Header
ID: 25930
DF = F, MF = T
Offset: 125
IP Payload
(Bytes 2000~3000)
IP Header
ID: 25930
DF = F, MF = F
Offset: 250
IP Payload
(Bytes 0~3000)
More Fragments = True
on all but the last fragment.
Don't Fragment = False allows us to fragment.
More Fragments = False
on the last fragment.
Offset measured in multiples of 8 bytes. 1000 / 8 = 125. 2000 / 8 = 250.
IP header size = 20 bytes, payload size = 1000 bytes. Extremely not to scale.
Same ID on each fragment of this packet.

## Slide 63: Task #6: Specify Special Packet Handling
Type of Service: Treat packets differently depending on application/customer needs.
Options: Request advanced functionality for this packet.
Version (4) | Hdr len (4) | Type of Service (8) |  | Total Length in Bytes (16) |  |  | 
Identification (16) |  |  |  | Flags (3) | Fragment Offset (13) |  | 
TTL (8) |  | Protocol (8) |  | Header Checksum (16) |  |  | 
Source IP Address (32) |  |  |  |  |  |  | 
Destination IP Address (32) |  |  |  |  |  |  | 
Options (if any) |  |  |  |  |  |  | 
Payload |  |  |  |  |  |  | 

## Slide 64: Task #6: Specify Special Packet Handling
Type of Service: Treat packets differently depending on application/customer needs.
Original idea:
Request different forms of delivery depending on these bits.
Based on priority, delay, throughput, reliability, cost, etc.
These bits were frequently re-defined and never fully deployed.
Only the notion of priorities remained.
Modern usage:
Differentiated Services Code Point (DSCP): Defines "classes" of traffic.
Explicit Congestion Notification (ECN): Used in congestion control (coming soon).

## Slide 65: Task #6: Specify Special Packet Handling
Options: Request advanced functionality for this packet.
Examples:
Record Route: Tell me the path that this packet took (useful for diagnostics).
Source Route: Send the packet along the route I provide.
Timestamp: Record when each router processes this packet.
Options lead to more complex implementation.
Options are variable-length, so routers have to check header length.
Higher processing overhead for routers.
On the modern Internet, we avoid options when possible.

## Slide 66: Introducing the IP Header
Version (4) | Hdr len (4) | Type of Service (8) |  | Total Length in Bytes (16) |  |  | 
Identification (16) |  |  |  | Flags (3) | Fragment Offset (13) |  | 
TTL (8) |  | Protocol (8) |  | Header Checksum (16) |  |  | 
Source IP Address (32) |  |  |  |  |  |  | 
Destination IP Address (32) |  |  |  |  |  |  | 
Options (if any) |  |  |  |  |  |  | 
Payload |  |  |  |  |  |  | 
Parse the packet. (both router and destination)
Forward packet to the next hop. (router only)
Tell the destination what to do next. (destination only)
Send responses back to the source. (both router and destination)
Handle errors. (both router and destination)
Specify any special packet handling. (both router and destination)

## Slide 67: IPv6 Changes
BGP Implementation
External BGP and Internal BGP
Multiple Links Between ASes
Message Types and Route Attributes
Issues with BGP
IP Header
IPv4 Header Fields
IPv6 Changes
Security
Lecture 9, Spring 2026

## Slide 68: Why IPv6?
Main motivation: IP address exhaustion.
IPv4 addresses are 32 bits long. There are 232 ≈ 4.2 billion IPv4 addresses. We're running out of IPv4 addresses.
IPv6 addresses are 128 bits long. 2128 > number of atoms in the universe. We won't run out.
Took the opportunity to modernize (update or remove) outdated fields.
Notes: IPv6 was originally supposed to be more ambitious, but additional features were never realized.
The result is an elegant, if unambitious, protocol.

## Slide 69: Cleanup #1: Eliminate Checksums
IPv6 eliminates checksums in the IP header.
Benefit of checksum:
  If a packet is corrupted but not detected, we keep sending it, which wastes bandwidth.
  Checksum lets us drop the packet early.
Why IPv6 made the change:
  Today, bandwidth is less of a bottleneck.
  It's okay if a few corrupt packets are sent through the network.
Benefit of no checksum:
  Less work for routers to do. Routers can process packets faster.

## Slide 70: Cleanup #2: Eliminate Fragmentation
IPv6 eliminates fragmentation.
If a packet is too large for a link:
  Drop the packet.
  Send an error back to the source with the maximum packet size (MTU).
  It's the sender's job to split up data into smaller packets.
Benefit of this change:
  Less work for routers to do. Routers can process packets faster.

## Slide 71: Cleanup #3: Eliminate Options
IPv6 eliminates options.
IP header is now fixed size.
Benefit: Less work for routers to do. Routers can process packets faster.
Replacement mechanism: Next Header.
Generalization of the IPv4 Protocol field.
If you want extra processing, put the protocol ID in the Next Header field.
IPv6 will pass the packet to the protocol for extra processing.
When the extra processing is done, the protocol passes the packet to Layer 4.
IPv6 Header
Next Header = 43
Bonus Header
TCP Header
TCP Payload

## Slide 72: Cleanup #3: Eliminate Options
Next Header can be generalized to multiple extra protocols in between Layer 3 and 4.
IPv6 and the extra protocols all include a Next Header field to pass the packet to the appropriate next protocol.
Eventually, someone's Next Header is a Layer 4 protocol (6 = TCP, 17 = UDP).
Future-proofing: Elegant way to support new protocols as they're invented.
IPv6 Header
Next Header = 43
Bonus Header
Next Header: 6
TCP Header
TCP Payload
Bonus Header
Next Header: 51

## Slide 73: Cleanup #4: Flow Label
The flow label field lets us denote when packets are related to each other.
Original Layer 3 design:
  Every packet is sent independently.
  Only higher layers need to think about grouping packets into flows.
Why IPv6 made the change:
  Modern routers often install middlebox systems to peek at IP packets, even if the router is not the destination.
  Example: Firewall on the router peeks at packets to block malicious traffic.
  Middleboxes might want to consider packets in a flow together.
  Flow label gives us a way to tell middleboxes when packets are related.

## Slide 74: IPv4 → IPv6 Header
Eliminate checksums.
Eliminate fragmentation.
Eliminate options, add next header.
Add flow label.
Version | Hdr len | Type of Service |  | Total Length in Bytes |  |  | 
Identification |  |  |  | Flags | Fragment Offset |  | 
TTL |  | Protocol |  | Header Checksum |  |  | 
Source IP Address (32 bits) |  |  |  |  |  |  | 
Destination IP Address (32 bits) |  |  |  |  |  |  | 
Options (if any) |  |  |  |  |  |  | 
Payload |  |  |  |  |  |  | 
Vers | Traffic Class |  | Flow Label |  |  |  | 
Payload Length |  |  |  | Next Header |  | Hop Limit | 
Source IP Address (128 bits) |  |  |  |  |  |  | 
Destination Address (128 bits) |  |  |  |  |  |  | 
Renamed and moved:
Type of Service → Traffic Class
Total Length → Payload Length
TTL → Hop Limit

## Slide 75: Philosophy of IPv6 Changes
Leave problems to end hosts.
Eliminated fragmentation.
Eliminated checksum.
Could we eliminate TTL and leave that to end hosts?
  No, avoiding loops is fundamentally a router problem.
Simplify: Less work for routers.
Eliminated options.
Fixed-size header length.
Future-proof: Allow for extensibility.
Generalized next-header approach.
Generalized flow label for packets.

## Slide 76: IP Security
BGP Implementation
External BGP and Internal BGP
Multiple Links Between ASes
Message Types and Route Attributes
Issues with BGP
IP Header
IPv4 Header Fields
IPv6 Changes
Security
Lecture 9, Spring 2026

## Slide 77: Exploiting Source IP: Spoofing
Spoofing: Lie about the source address.
Attacker pretends to be somebody else and sends the packet.
Using spoofing to attack a destination:
Denial-of-service (DoS) attack: Overwhelm a service by flooding it with packets.
Without spoofing: The service can block your source address.
Spoofing makes DoS more effective: Server doesn't know which packets to block.
Using spoofing to attack the impersonated user:
Attacker pretends to be Bob and sends a virus.
Now Bob is wrongly blamed for sending the virus.
Return traffic (e.g. angry messages) goes to Bob instead.

## Slide 78: Exploiting Type of Service
Recall type of service (ToS): Bits indicating priority of the packet.
Attack: Prioritize your own traffic.
If anybody can set ToS bits, attackers can make their own packets high-priority.
Network prefers attacker traffic.
Today, ToS bits are mostly set/used by operators, not end hosts.
Attack: Use spoofing to make someone else pay for priority traffic.
Suppose the network charges for high-priority traffic.
Attacker sends a spoofed packet: "I am Bob and this packet is high-priority."
Network makes Bob pay for that packet.

## Slide 79: Exploiting Fragmentation and Options
Recall: Fragmentation and options are more work for the router.
Denial-of-service (DoS) attack: Overwhelm routers by making them do more work.
Fragmentation: Send large packets on purpose, causing many fragments.
Options: Send packets with complicated options on purpose.
  Defense: Routers often ignore options, or drop packets with options.

## Slide 80: Exploiting TTL: Traceroute
Traceroute: Exploiting the TTL to discover the path a packet travels along.
Key idea: When TTL expires, the router sends back a "TTL Exceeded" error. This allows you to learn the identity one of the routers on the path.
Basic approach: Send packets with TTL=1, TTL=2, TTL=3, etc.
A
B
C
S
T
From: S To: T
TTL = 1
From: A To: S
TTL Exceeded
A
B
C
S
T
From: S To: T
TTL = 2
From: B To: S
TTL Exceeded
A
B
C
S
T
From: S To: T
TTL = 3
From: C To: S
TTL Exceeded
Notes: Not all routers respond with the "TTL Exceeded" message.

## Slide 81: Exploiting Other Fields?
Exploiting protocol field?
If protocol is set incorrectly, the next layer will find the packet malformed.
Exploiting checksum?
A bad checksum causes the network to drop the packet.
These are not effective attacks.

## Slide 82: Summary of IP Attacks
Source IP address: Spoofing.
Type of service: Prioritize attacker traffic.
Fragmentation, Options: Denial-of-service.
TTL: Traceroute.
Protocol, Checksum: No apparent problems.
Version | Hdr len | Type of Service |  | Total Length in Bytes |  |  | 
Identification |  |  |  | Flags | Fragment Offset |  | 
TTL |  | Protocol |  | Header Checksum |  |  | 
Source IP Address (32 bits) |  |  |  |  |  |  | 
Destination IP Address (32 bits) |  |  |  |  |  |  | 
Options (if any) |  |  |  |  |  |  | 
Payload |  |  |  |  |  |  | 

## Slide 83: Recap: IP Header Design
Header design is more nuanced than it first seems!
We have to juggle multiple goals:
Efficient implementation
Security
Future needs