## Slide 1
TCP Implementation
Lecture 11 (Transport 2)
...
...
...
...
...
...
...
...
..
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
Notes: Slides template credit: Josh Hug, Lisa Yan
today is the second half of the TCP implementation lecture and we're
0:45
going to take what we saw last time the ideas that we Ed to design reliability
0:50
and we're going to formalize them into an actual protocol
And if we have time we might also do some congestion control to get ahead on that

## Slide 2: Implementing TCP: Byte Notation (Segments, Sequence Numbers)
Implementing TCP
Byte Notation (Segments, Sequence Numbers)
Maintaining State (Full Duplex, Connection Setup and Teardown)
Sliding Window
Header
Lecture 11, CS 168, Summer 2025
Notes: 1:03
TCP and the first thing we'll do is we'll take the packet view of TCP and change it to a bite view

## Slide 3: Notation Change: Bytes vs. Packets
So far, we've used packets as the primary unit of data.
Each packet has a number.
Acks reference packet numbers.
Window size expressed in terms of number of packets.
TCP is implemented with bytes as the primary unit of data.
Each byte has a number. Packets are defined by the number of the first byte inside.
ACKs reference byte numbers.
Window size expressed in terms of number of bytes.
You should be prepared to reason in terms of either.
Notes: Packets different sizes

## Slide 4: TCP Segments
TCP provides a reliable, in-order bytestream.
We have to split this bytestream into packets.
Byte 1
Byte 2
Byte 3
Byte 4
...
...
...
Byte 79
Byte 80
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
Sender Application
Byte 1
Byte 2
Byte 3
Byte 4
...
...
...
Byte 79
Byte 80
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
Recipient Application
Notes: the B stream that we talked about and remember the bite stream is a sequence of bytes in order
3:33
infinite length the sender has a bite stream we feed it into a pipe and then the recipient receives those exact same
3:40
bytes in the same order reliably now the only difference between this picture and
3:46
the ones you've previously seen is that I have stamped numbers on every single
3:52
bite so now we have to connect this picture with the packet picture from last time and this is how we'll square
3:59
the two pictures together so the way that you build a packet as byes come in
4:05
and remember the sender application doesn't have to give you the entire infinite length by stream at once it
4:11
could feed you the bytes one by one for example if it's Computing data and it's sending out any results that it computes

## Slide 5: TCP Segments
TCP Segment
A segment is sent when the segment is full (max segment size),
or when the segment is not full, but times out waiting for more data.
Byte 1
Byte 2
Byte 3
Byte 4
...
...
...
Byte 79
Byte 80
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
Sender Application
TCP Segment
Byte 1
Byte 2
Byte 3
Byte 4
...
...
...
Byte 79
Byte 80
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
Recipient Application
TCP
HDR
TCP
HDR
TCP header carries a sequence number indicating where in the bytestream this segment fits.

## Slide 6: TCP Segments
TCP/IP packet: IP packet with TCP header and TCP data inside.
Size limits:
IP packet: Maximum transmission unit (MTU).
TCP segment: Maximum segment size (MSS).
MSS = MTU – (IP header) – (TCP header).
TCP Header
TCP Payload (Segment)
IP Header
IP Payload
Limit MTU bytes
Limit MSS bytes
Notes: so packets larger than the MTU will get fragmented and we don't want that so we
6:53
will say the IP packet is limited to MTU bites and to figure out how big one of
6:59
these segments can be we just have to do some math this whole thing can be up to MTU bytes that's a limit that's set on
7:06
the Internet it's 1500 in real life but some of it's being used for the IP header so we have to subtract that off
7:13
and some of it's being used for the TCP header so we subtract that off and whatever is left that number is MSS that

## Slide 7: TCP Sequence Numbers
Numbering starts at a randomly-generated Initial Sequence Number (ISN).
First byte is ISN+1, then ISN+2, etc.
Starting at a randomly-chosen ISN is very important for security!
ISN + 1
ISN + 2
ISN + 3
ISN + 4
...
...
...
ISN + 79
ISN + 80
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
ISN + 1
ISN + 2
ISN + 3
ISN + 4
...
...
...
ISN + 79
ISN + 80
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
Recipient Application
Sender Application
Notes: here's one thing we haven't talked about that is important for security and that is the
7:56
fact that sequence numbers actually shouldn't start at zero if you want to know why the security course cs161 goes
8:02
into a lot more detail of why this is the case but just know for this class that there is a very important security
8:09
reason and for that reason we cannot start the counting at zero instead we
8:14
have to pick some random number and here we'll call it Isn initial sequence number and then just start at that
8:21
number and start counting up so if that number is 120 okay great then the first bite is 121 and then 122 and then 123
8:30
and then 124 and so on this doesn't really change anything we've talked about so far it's still a bite stream
8:37
and you're still counting the bytes all the way up the only difference is don't start counting from zero that's the only
8:44
difference and it doesn't change any of the other implementation details but

## Slide 8: TCP Sequence Numbers
TCP Segment
The sequence number of a segment is the number of the first byte in the segment.
Example: In the segment below, the sequence number is ISN + 140.
ISN + 1
ISN + 2
ISN + 3
ISN + 4
...
...
...
ISN + 79
ISN + 80
...
...
...
...
...
...
...
ISN+140
ISN+141
ISN+142
ISN+143
...
...
...
ISN+218
ISN+219
...
...
...
...
...
...
...
...
...
...
...
TCP Segment
ISN + 1
ISN + 2
ISN + 3
ISN + 4
...
...
...
ISN + 79
ISN + 80
...
...
...
...
...
...
...
ISN+140
ISN+141
ISN+142
ISN+143
...
...
...
ISN+218
ISN+219
...
...
...
...
...
...
...
...
...
...
...
Recipient Application
TCP
HDR
TCP
HDR
Sender Application

## Slide 9: TCP Ack Numbers
TCP Segment
The ack number indicates the next expected byte (i.e. the first unreceived byte).
Example: All bytes up to (and including) ISN + 219 have been received, so the next unreceived byte is ISN + 220.
ISN + 1
ISN + 2
ISN + 3
ISN + 4
...
...
...
ISN + 79
ISN + 80
...
...
...
...
...
...
...
ISN+140
ISN+141
ISN+142
ISN+143
...
...
...
ISN+218
ISN+219
...
...
...
...
...
...
...
...
...
...
...
Sender Application
TCP Segment
ISN + 1
ISN + 2
ISN + 3
ISN + 4
...
...
...
ISN + 79
ISN + 80
...
...
...
...
...
...
...
ISN+140
ISN+141
ISN+142
ISN+143
...
...
...
ISN+218
ISN+219
...
...
...
...
...
...
...
...
...
...
...
Recipient Application
TCP
HDR
TCP
HDR
Ack: ISN + 220.

## Slide 10: TCP Sequence and Ack Numbers
The sequence number of a segment is the number of the first byte in the segment.
Sender sends a packet with sequence number j.
The packet contains B bytes.
Bytes in the packet are numbered: j, j+1, j+2, j+3, ..., , j+B–1.
Recipient sends a cumulative ack (number of highest byte received, plus one).
If all prior data is received, ack number is j+B.
Think of this as the next expected byte, or the first unreceived byte.
If earlier data before this packet is missing, the ack number will be lower.

## Slide 11: TCP Sequence and Ack Numbers
Assuming only one packet in flight, all packets length B, and no loss:
The last ack number is equal to the next sequence number.
"I expect j + B next." → "I'm sending j + B."
Sender
Recipient
ack = j + B
seq = j
seq = j + B
ack = j + 2B
seq = j + 2B

## Slide 12: Maintaining State (Full Duplex)
Implementing TCP
Byte Notation (Segments, Sequence Numbers)
Maintaining State (Full Duplex, Connection Setup and Teardown)
Sliding Window
Header
Lecture 11, CS 168, Summer 2025

## Slide 13: TCP State
Reliability requires maintaining state at the end hosts.
Sender has to remember:
  Which packets have been sent and not acked?
  How much longer on the timer before I resend a packet?
Receiver has to buffer the out-of-order packets.
State is maintained at the end hosts, not in the network.
In each separate connection, both end hosts need to maintain state.

## Slide 14: TCP is Full-Duplex
So far, we defined a sender and a recipient in every connection.
Connections in TCP are full-duplex.
Both hosts can send data, and both hosts can receive data.
A can send to B, and B can send to A, simultaneously, in the same connection.
To support full-duplex connections:
Two sets of sequence numbers: One for A→B bytes, and one for B→A bytes.
Each packet carries both data and ack information.
  "Here are some bytes starting at 15..."
  "...Also, I ack receiving all your bytes up to (not including) 84."
15 | 16 | 17 | 18 | 19 | 20 | 21
H | e | l | l | o | , | B
77 | 78 | 79 | 80 | 81 | 82 | 83
H | e | l | l | o | , | A
A to B bytestream
B to A bytestream

## Slide 15: TCP Connection Setup: Three-Way Handshake
Goal: Each host tells its ISN to the other host.
SYN. Client says: "Here's my ISN."
SYN-ACK. Server says: "I received your ISN. Also, here's my ISN."
ACK. Client says: "I received your ISN."
After the three-way handshake, both sides can start sending data.
SYN-ACK
Client
Server
SYN
ACK

## Slide 16: TCP Connection Setup: Three-Way Handshake
Goal: Each host tells its ISN to the other host.
SYN. Client says: "My ISN is x."
SYN-ACK. Server says: "I received x (expecting x+1 next). Also, my ISN is y."
ACK. Client says: "I received y (expecting y+1 next)."
After the three-way handshake, both sides can start sending data.
SYN-ACK. seq=y, ack=x+1
Client
Server
SYN. seq=x
ACK. ack=y+1

## Slide 17: TCP Connection Teardown
Normal termination:
Each side sends a FIN packet to say: "I'm done sending, but will keep receiving."
FIN packets must be acked, just like any other data.
When only one side has sent FIN, the connection is half-closed.
When both sides have sent FIN (both done sending), the connection is closed.
ACK
Client
Server
FIN
ACK
FIN

## Slide 18: TCP Connection Teardown
Abrupt termination can be used instead (e.g. in case of error).
Send a RST (reset) to say: "I will no longer send or receive data."
RST packets do not need to be acked.
Any data in flight is lost.
If the RST sender receives more data later, send another RST.
Client
Server
RST
data
RST

## Slide 19: TCP Setup/Teardown Transition Diagram
ESTABLISHED
CLOSE_WAIT
LAST_ACK
CLOSED
TIME_WAIT
CLOSING
FIN_WAIT_2
FIN_WAIT_1
SYN_RCVD
LISTEN
CLOSED
SYN_SENT
FIN/ACK
ACK + FIN/ACK
ACK
Timeout after 2 segment lifetimes
ACK
Close/FIN
FIN/ACK
ACK
Close/FIN
Close/FIN
ACK
FIN/ACK
SYN+ACK/ACK
SYN/SYN+ACK
SYN/SYN+ACK
Send/SYN
Close
Close
Passive open
Active open/SYN
The ESTABLISHED state is where all data is sent and acked.

## Slide 20: TCP Setup/Teardown Transition Diagram (Simplified)
FIN_WAIT1
FIN_WAIT2
ESTABLISHED
CLOSED
TIME_WAIT
SYN_SENT
Send SYN
Receive SYN+ACK
Send ACK
Send FIN
Receive ACK
Receive FIN
Send ACK
Wait a while
Setup
Teardown

## Slide 21: Piggybacking
With full-duplex, if we get a packet but have no data to send, we have two choices:
Send the ack, with no data.
Piggybacking: Wait for some data, and send the ack with the data.
Piggybacking can be tricky because TCP is in the OS, separate from the application.
OS doesn't know when application will have more data.
Application isn't thinking about packets and acks.
SYN-ACKs are always piggybacked.
Ack and initial sequence number are sent together.
Not tricky, because OS is doing the handshake, not the application.

## Slide 22: Sliding Window
Implementing TCP
Byte Notation (Segments, Sequence Numbers)
Maintaining State (Full Duplex, Connection Setup and Teardown)
Sliding Window
Header
Lecture 11, CS 168, Summer 2025

## Slide 23: TCP Sliding Window
...
3
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
31
32
33
34
35
36
37
38
39
40
...
...
1
2
4
5
Sent and acked
6
7
Not sent yet
Window
W bytes
First unacked byte
When we measured in packets, W was the maximum number of packets in flight.
When we measure in bytes, W is the maximum number of contiguous bytes in flight.
The window is a range of W contiguous bytes, starting at the first unacked byte.
Only these W bytes are allowed to be in flight.
The window slides right if and only if its leftmost bytes are acked.
Example: When 15–18 arrive, we can send 27–30.

## Slide 24: TCP Sliding Window
...
3
When we measured in packets, W was the maximum number of packets in flight.
When we measure in bytes, W is the maximum number of contiguous bytes in flight.
The window is a range of W contiguous bytes, starting at the first unacked byte.
Only these W bytes are allowed to be in flight.
The window slides right if and only if its leftmost bytes are acked.
Example: When 15–18 arrive, we can send 27–30.
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
31
32
33
34
35
36
37
38
39
40
...
...
1
2
Sent and acked
4
5
6
7
Not sent yet
Window
W bytes
First unacked byte

## Slide 25: TCP Sliding Window
...
3
When we measured in packets, W was the maximum number of packets in flight.
When we measure in bytes, W is the maximum number of contiguous bytes in flight.
The window is a range of W contiguous bytes, starting at the first unacked byte.
Only these W bytes are allowed to be in flight.
The window slides right if and only if its leftmost bytes are acked.
Acking non-leftmost bytes in the window (e.g. 19–22) does not slide the window.
The window is determined by the first unacked byte (e.g. still 15).
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
31
32
33
34
35
36
37
38
39
40
...
...
1
2
Sent and acked
4
5
6
7
Not sent yet
Window
W bytes
First unacked byte

## Slide 26: TCP Sliding Window
TCP uses cumulative acks and a sliding window.
Cumulative ack: "I have received everything up to (not including) 15."
Thus, first unacked byte is 15, and the sliding window is [15, 15 + W).
W is set as the minimum of two values:
Advertised window (recipient reports their remaining buffer space).
Congestion window (sender magically finds value to avoid network overload).
...
3
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
31
32
33
34
35
36
37
38
39
40
...
...
1
2
4
5
Sent and acked
6
7
Not sent yet
Window
W bytes
First unacked byte

## Slide 27: Detecting Loss
Two ways to detect loss and resend. We resend if either condition is true.
In both cases, we always resend the first unacked packet (leftmost part of window).
Ack-based: If 3 duplicate acks are received, resend.
Timer-based: Keep a single timer. If the timer expires, resend.
  Different from packet-based TCP, where we kept one timer per packet.
  Set timer by estimating RTT (e.g. measure times between packets and acks, and take a moving average).
...
3
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
31
32
33
34
35
36
37
38
39
40
...
...
1
2
4
5
Sent and acked
6
7
Not sent yet
Window
W bytes
Resend 15–18 if timer expires, or if 3 copies of ack(15) received.

## Slide 28: TCP Header
Implementing TCP
Byte Notation (Segments, Sequence Numbers)
Maintaining State (Full Duplex, Connection Setup and Teardown)
Sliding Window
Header
Lecture 11, CS 168, Summer 2025

## Slide 29: TCP Header
What functions does TCP implement?
Demultiplexing (ports)
Reliability (checksum, sequence and ack numbers)
Connection setup and teardown (flags)
Flow control (advertised window)
Source Port (16) |  |  |  | Destination Port (16) |  |  | 
Sequence Number (32) |  |  |  |  |  |  | 
Acknowledgment Number (32) |  |  |  |  |  |  | 
Hdr Len (4) | 0000 | Flags (8) |  | Advertised Window (16) |  |  | 
Checksum (16) |  |  |  | Urgent Pointer (16) |  |  | 
Options (variable-length) |  |  |  |  |  |  | 
Payload |  |  |  |  |  |  | 

## Slide 30: TCP Header
There are 8 flags that can be set in TCP. We care about 4 of them:
SYN: I'm sending my initial sequence number.
ACK: I'm acking data (please look at the ack number).
FIN: I'm done sending data, but will keep receiving data.
RST: I'm done sending and receiving data.
We won't look at the other four: CWR, ECE, URG, PSH.
Source Port (16) |  |  |  | Destination Port (16) |  |  | 
Sequence Number (32) |  |  |  |  |  |  | 
Acknowledgment Number (32) |  |  |  |  |  |  | 
Hdr Len (4) | 0000 | Flags (8) |  | Advertised Window (16) |  |  | 
Checksum (16) |  |  |  | Urgent Pointer (16) |  |  | 
Options (variable-length) |  |  |  |  |  |  | 
Payload |  |  |  |  |  |  | 

## Slide 31: TCP Header
Remaining fields:
Header length: Measured in 4-byte words.
  If no options, this is 5 (header is 20 bytes long).
0000: Reserved bits (always set to 0).
Urgent pointer: Used with the URG flag to indicate urgent data. Won't discuss.
Options: Extra functionality.
  Example: SACK uses the options field to implement full-information acks.
Source Port (16) |  |  |  | Destination Port (16) |  |  | 
Sequence Number (32) |  |  |  |  |  |  | 
Acknowledgment Number (32) |  |  |  |  |  |  | 
Hdr Len (4) | 0000 | Flags (8) |  | Advertised Window (16) |  |  | 
Checksum (16) |  |  |  | Urgent Pointer (16) |  |  | 
Options (variable-length) |  |  |  |  |  |  | 
Payload |  |  |  |  |  |  | 

## Slide 32: TCP: Summary
An elegant (though not perfect) piece of engineering that has stood the test of time.
Thought experiment: Will TCP continue to be a good solution?
Plenty of evolution in individual pieces:
Congestion control was added after-the-fact.
Better acknowledgments, ISN selection, timer estimation, etc.
But the core architectural decisions and abstractions remain:
Bytestreams, connection-oriented, windows, etc.
Vint Cerf and Bob Kahn have won basically every award ever for their work on TCP.

## Slide 33
CS 168, Summer 2025 @ UC Berkeley
Slides credit: Sylvia Ratnasamy, Rob Shakir, Peyrin Kao
Congestion Control, Part 1
Lecture 12 (Transport 3)
Notes: Slides template credit: Josh Hug, Lisa Yan
Copied here just in case we get there!

## Slide 34: Congestion Control: Why do we need it?
Congestion Control Principles
Why do we need it?
Why is it hard?
Design Goals
Dynamic Adjustment
Algorithm Sketch
Reacting to Congestion (AIMD)
Implementing Congestion Control with Event-Driven Updates
Lecture 12, CS 168, Summer 2025

## Slide 35: Recall: Congestion at Routers
If two packets arrive at the same time, the router will send one, and buffer the other.
The router maintains a queue of packets that still need to be sent.
If the queue is full, and a packet arrives, the packet gets dropped.
If too many packets arrive close in time:
The router cannot keep up, and gets congested.
Packets can be delayed (stuck waiting in queue) or dropped (queue is full).
B
A
Router
I cannot send both A and B right now.
One of them will have to wait.

## Slide 36: Congestion Delays Packets
For a typical queuing system with bursty arrivals:
Higher load = more packets sent = higher packet delay.
Delay gets really bad, even before we reach 100% load.
Trade-offs: Need to balance high link utilization and low delay.
Load
100% load
Average Packet Delay

## Slide 37: Brief History of Congestion Control
In the 1980s, TCP did not implement congestion control.
Sending rate was only limited by flow control (recipient buffer capacity).
If packets are dropped, resend them over and over, at the same fast rate.
This led to a congestion collapse.
1986: Capacity of a major link dropped to 0.1% of its original capacity.
Why? Network was flooded with thousands of copies of every packet.
In October of '86, the Internet had the first of what became a series of 'congestion collapses.' During this period, the data throughput from LBL to UC Berkeley (sites separated by 400 yards and two IMP hops) dropped from 32 Kbps to 40 bps. We were fascinated by this sudden factor-of-thousand drop in bandwidth and embarked on an investigation of why things had gotten so bad. In particular, we wondered if the 4.3BSD (Berkeley Unix) TCP was mis-behaving or if it could be tuned to work better under abysmal network conditions. The answer to both of these questions was "yes".
– Karels (UCB) and Jacobson (LBL)

## Slide 38: Brief History of Congestion Control
How was congestion collapse solved in the 1980s?
Michael Karels and Van Jacobson were working on BSD (an early OS).
They changed a few lines of TCP code to fix the problem.
  Recall: TCP is implemented in everybody's OS.
  The fix worked, and everybody quickly adopted it.
The history of congestion control had a big impact on its design.
Invented as an ad-hoc patch to an existing system. (Not in original TCP design.)
Implemented in the OS. (Not in applications, routers, etc.)
Fast-forward to today:
Extensive research and improvements since the original patch.
The core ideas in the original patch still persist.
No major congestion collapses ever since.
Notes: Berkeley Software Distribution - Berkeley Unix

## Slide 39: Congestion Control: Why is it hard?
Congestion Control Principles
Why do we need it?
Why is it hard?
Design Goals
Dynamic Adjustment
Algorithm Sketch
Reacting to Congestion (AIMD)
Implementing Congestion Control with Event-Driven Updates
Lecture 12, CS 168, Summer 2025

## Slide 40: Congestion Control Challenges: Depends on Destination
At what rate should A send traffic?
It depends on the destination.
A → C can send at 10 Gbps.
A → F can only send at 2 Gbps.
A
B
R1
R3
R7
R4
R2
R5
R6
G
F
E
D
C
10
2
1
4
4
10
10
4
5
10
Numbers are bandwidths, in Gbps.
Ignore bandwidth of host-to-router links.

## Slide 41: Congestion Control Challenges: Depends on Path
At what rate should A → E send traffic?
It depends on the path through the network.
A → E via R3 can send at 10 Gbps.
A → E via R2 can send at 1 Gbps.
A
B
R1
R3
R7
R4
R2
R5
R6
G
F
E
D
C
10
2
1
4
4
10
10
4
5
10

## Slide 42: Congestion Control Challenges: Depends on Competing Flows
At what rate should A → F send traffic?
It depends on others using the network.
A → F and B → E share a link.
B → E can send at 1 Gbps.
A → F can send at 1 Gbps.
A
B
R1
R3
R7
R4
R2
R5
R6
G
F
E
D
C
10
2
1
4
4
10
10
4
5
10

## Slide 43: Congestion Control Challenges: Depends on Indirect Competition
What if G → D starts sending traffic?
Maybe B → E should slow to 0.5 Gbps.
Then A → F could increase to 1.5 Gbps.
G → D and A → F share no links, but they still affected each other's bandwidth.
A
B
G
F
E
D
C
10
2
1
4
4
10
10
4
5
10
R1
R3
R7
R4
R2
R5
R6

## Slide 44: Congestion Control is a Global Problem
The sender's optimal rate depends on:
The destination.
The path to the destination.
Other connections sharing links along that path.
Connections sharing links with those other connections.
And so on...
Congestion control is a global problem.
Connections in the network are highly interdependent.
Solving it optimally requires a global view of the network.

## Slide 45: Congestion Control as Resource Allocation Problem
Fundamentally, congestion control is a resource allocation problem.
Bandwidth is a limited resource.
Each connection demands a certain amount of bandwidth.
We decide how much to allocate to each connection.
Resource allocation is a classic problem (e.g. CPU scheduling, memory allocation).
But, congestion control has additional challenges.
A change in one connection can have a global impact.
Network topology is constantly changing.
Connections are constantly starting and ending.
Everybody must solve it locally. No global view of network.

## Slide 46: Design Goals
Congestion Control Principles
Why do we need it?
Why is it hard?
Design Goals
Dynamic Adjustment
Algorithm Sketch
Reacting to Congestion (AIMD)
Implementing Congestion Control with Event-Driven Updates
Lecture 12, CS 168, Summer 2025

## Slide 47: Design Goals
Goals for a good congestion control algorithm:
Avoid congestion: Minimize packet delay and loss.
Efficiency: Maximize link utilization.
Fairness: Connections should share the available bandwidth.
Practical to implement: Scalable, decentralized, adaptive, etc.
Our ultimate goal is a good tradeoff between these metrics.
Could avoid congestion (1) by sending really slowly.
But then we aren't using all the bandwidth on the link (2).

## Slide 48: Possible Approaches
Reservations:
Connections reserve bandwidth at the start, and release bandwidth at the end.
Requires connections to know bandwidth ahead of time.
Other problems: Hard to implement, inefficient bandwidth usage, etc.
Pricing/priorities:
Analogy: Express toll lanes on the highway. Price changes depending on traffic.
Prioritize traffic from users who pay more.
Requires a payment model.
Dynamic adjustment:
Learn the current congestion level, and adjust your rate accordingly.
Requires good citizenship (no cheating).

## Slide 49: Possible Approaches
3 possible approaches: reservations, pricing, and dynamic adjustment.
All the algorithms we'll see are based on dynamic adjustment.
If we rebuilt the Internet from scratch, another approach might be feasible.
But congestion control was invented as a patch on the existing Internet.
Dynamic adjustment is the best fit for the existing Internet:
  Doesn't require knowing bandwidth ahead of time.
  Doesn't require a payment model.
Congestion Control Protocols
Pricing
Reservations
Dynamic Adjustment