## Slide 1: Distance-Vector Algorithm Sketch
Distance-Vector Correctness
Algorithm Sketch
Rule 1: Bellman-Ford Updates
Bellman-Ford Demo
Rule 2: Updates From Next-Hop
Rule 3: Resending
Rule 4: Expiring
Distance-Vector Enhancements
Rule 5: Poison Expired Routes
Rule 6A: Split Horizon
Rule 6B: Poison Reverse
Rule 7: Count To Infinity
Eventful Updates
Lecture 5, Spring 2026
Notes: Welcome to week 2
Finally, we get to build a routing protocol. Today will be entirely focused on Distance-Vector approach and then we’ll talk about an alternative approach hopefully tomorrow.
so we're going to number them 1 through seven we'll come up with rules and when you put the seven rules together you get
29:30
an algorithm called the distance Vector protocol and it allows us to find shortest paths through the entire
29:36
network

## Slide 2: Distance-Vector Algorithm Sketch
One-line algorithm: If you hear about a path to a destination, tell all your neighbors.
R2
A
R3
R1
R5
R4
R6
R7
R8
R9
R10
R11
R12
R13
R14
R15
A is 1 away from me. I should tell my neighbors.
A this way
Notes: so let's Jump Right In so before we talk about any rules let me just give
29:41
you a one slide one sentence version of this algorithm so all you have to do is
29:47
that if you hear about a path to a destination tell all your neighbors that's the oneliner version of this
29:54
algorithm we're then going to spend a lot of time making it good but at a high level this is what it looks like so what
30:00
does that mean let's say R1 wakes up one day and it sees that it has a hardcoded route to a so remember we said that
30:08
static routes are the ones that are hardcoded if you're directly connected to a host then we will hardcode an entry
30:15
into r1's table saying that your next top to a is direct so R1 wakes up one
30:21
day with this hardcoded entry and says I know a way to get to a so you know what I should do I should spread the love I
30:27
should tell all of my neighbors that if they want to reach a they should come through me so R1 thinks I can reach a so
30:35
let me go tell all of my neighbors so that if they want to reach a they can come through me as well so that's what

## Slide 3: Distance-Vector Algorithm Sketch
One-line algorithm: If you hear about a path to a destination, tell all your neighbors.
R2
A
R3
R1
R5
R4
R6
R7
R8
R9
R10
R11
R12
R13
R14
R15
A this way
A is 1 away from me.
A is 1 away from me.
Notes: 30:40
R1 does R1 go goes ahead and tells all of its neighbors hey everyone I am R1
30:46
and I can reach a so if you ever want to talk to a send it to me and I got it for
30:51
you I'll send it to a for you so R2 and R3 hear this and now they can update their forwarding tables therefore in
30:58
table say if I want to send a packet to a I should forward it to R1 because R1
31:03
just told me that they can reach a

## Slide 4: Distance-Vector Algorithm Sketch
One-line algorithm: If you hear about a path to a destination, tell all your neighbors.
R2
A
R3
R1
R5
R4
R6
R7
R8
R9
R10
R11
R12
R13
R14
R15
A this way
We just found a way to reach A. We should tell our neighbors.
A this way
A this way
Notes: and likewise R3 thinks and says well I just heard this message from R1 saying they
31:10
can reach a so if I ever want to send packets to a I should just forward packets to R1 because they told me that
31:16
they can reach a so R2 and R3 can now program their forwarding tables with a path to a and because R2 and R3 can now
31:24
reach a they should also spread the love and tell their neighbors so R2 and R3 say we now know how to reach a let's
31:31
tell all of our neighbors how to reach a so that they can also join in on the fun and send packets to a

## Slide 5: Distance-Vector Algorithm Sketch
One-line algorithm: If you hear about a path to a destination, tell all your neighbors.
R2
A
R3
R1
R5
R4
R6
R7
R8
R9
R10
R11
R12
R13
R14
R15
A this way
A is 2 away from me.
A is 2 away.
A is 2 away.
A is 2 away.
A this way
A this way
Notes: so R2 and R3 send
31:39
packets to all of their neighbors and they say I can reach a as well so if you ever want to send packets to a send it
31:45
my way and R4 R5 R6 R7 they all hear

## Slide 6: Distance-Vector Algorithm Sketch
One-line algorithm: If you hear about a path to a destination, tell all your neighbors.
R2
A
R3
R1
R5
R4
R6
R7
R8
R9
R10
R11
R12
R13
R14
R15
A this way
We just found a way to reach A. We should tell our neighbors.
A this way
A this way
A this way
A this way
A this way
A this way
Notes: 31:51
this message saying R2 can reach a and R3 can reach a so now they can also
31:56
program entries into their forwork table so R4 says well R2 claims they can reach
32:01
a so if I ever want to talk to a I should send packets that way and R5 here
32:07
is well R2 says they can reach a so if I ever want to send packets to a I will send them this way and the same thing

## Slide 7: Distance-Vector Algorithm Sketch
One-line algorithm: If you hear about a path to a destination, tell all your neighbors.
R2
A
R3
R1
R5
R4
R6
R7
R8
R9
R10
R11
R12
R13
R14
R15
A this way
A this way
A this way
A this way
A this way
A this way
A this way
A is 3 away.
A is 3 away.
A is 3 away.
A is 3 away.
A is 3 away.
A is 3 away.
A is 3 away.
A is 3 away.
Notes: 32:28
they should also spread the love and tell their neighbors so their neighbors can also reach a so they talk to all
32:34
their neighbors saying I can reach a if you ever want to talk to a come through me and these routers can now program
32:40
routes through a as well and if you do this enough times that you spread the love all across the network eventually
32:47
everyone should have a forwarding table entry that points toward a these blue arrows form a valid directed delivery
32:54
tree where all the arrows Point toward a and now regardless of who's sending packets anywhere all these routers can
33:00
coordinate and send the packets toward a so at a very high level with a single line this is what you're supposed to do

## Slide 8: Distance-Vector Algorithm Sketch
One-line algorithm: If you hear about a path to a destination, tell all your neighbors.
R2
A
R3
R1
R5
R4
R6
R7
R8
R9
R10
R11
R12
R13
R14
R15
A this way
A this way
A this way
A this way
A this way
A this way
A this way
A this way
A this way
A this way
A this way
A this way
A this way
A this way
A this way
We did it! Everybody knows the next-hop to A now.

## Slide 9: Distance-Vector Algorithm Sketch – Routing vs. Forwarding
R2
A
R3
R1
R5
R4
R6
R7
R8
R9
R10
R11
R12
R13
R14
R15
Routing announcements ("I can reach A") propagated outward, away from A.
When forwarding packets toward A, packets travel inward, toward A.
Notes: remember there is a critical difference between routing and
34:36
forwarding and remember routing is the process of all the routers talking to each other to form uh valid forwarding
34:45
tables and forwarding is the process of receiving a packet from a user and using
34:50
the table to forward packets so routing is building the tables forwarding is using the tables that you just built
34:58
and something you'll notice if you look at the demo is that the direction of packets being sent in routing and
35:04
forwarding are opposites and this always trips people up so notice that when
35:09
everyone was sharing information with their friends about the fact that they can reach a that information propagated
35:16
outwards so it started at a and R1 at first these were the only two people who knew about a but slowly that information
35:24
radiated outwards and from a going F further and further and further away from a from the left side of your screen
35:31
to the right side of your screen propagating outwards from a until everyone knew the information by
35:37
contrast when you are forwarding when you actually have the tables filled in and you're ready to use the tables when
35:44
someone sends you a packet and says please forward this packet toward a then the packets travel inwards toward a

## Slide 10: Distance-Vector Algorithm Sketch – Multiple Destinations
What if there are multiple destinations?
Run the same path propagation algorithm, once per destination.
Routers use forwarding tables to keep track of the next-hop of each destination.
We'll focus on a single destination for simplicity.
But the protocol can extend to multiple destinations.

## Slide 11: Rule 1: Bellman-Ford Updates
Distance-Vector Correctness
Algorithm Sketch
Rule 1: Bellman-Ford Updates
Bellman-Ford Demo
Rule 2: Updates From Next-Hop
Rule 3: Resending
Rule 4: Expiring
Distance-Vector Enhancements
Rule 5: Poison Expired Routes
Rule 6A: Split Horizon
Rule 6B: Poison Reverse
Rule 7: Count To Infinity
Eventful Updates
Lecture 5, CS 168, Spring 2026
Notes: Pause to see if anyone can think of multipath, or expiring issues or other issues with the sketch

## Slide 12: Multiple Paths Advertised
What if you hear about multiple paths to a single destination?
Accept the shorter path.
R5
R3
R4
R2
R1
A
A is 3 away from me.
A is 2 away from me.
I prefer what R4 is offering.
A this way
Notes: 38:40
in the picture we showed you earlier everything was nice there was only a single path so when you heard about the
38:46
way to reach a you just pointed your forwarding table in the direction toward a but that might not always be the case
38:54
sometimes there are multiple paths to reach a destination so in this example as before R1 is the only one that knows
39:01
about a at the very beginning so it tells all its friends it tells R2 and R4
39:06
and then R2 tells R3 and then R3 tells R5 and then R4 tells R5 so what happened
39:13
here is R3 and R4 both have a way to reach a so R5 is going to hear two
39:20
different paths R3 is going to say I can reach a if you send packets to me I'll get to a but R4 will also say if you
39:28
send packets to me I will also re J so R5 now has a choice it can either
39:33
program its forwarding table to go via R3 or to go via R4 the next top to a
39:39
could either be R3 or R4 there's a choice and remember we said that both of these would be valid paths they would
39:46
send packets to a but one of them is better than the other in other words the cost is less and ultimately we want the
39:53
least cost path so what R5 should really do is prefer the path with less cost

## Slide 13: Multiple Paths Advertised
What if you hear about multiple paths to a single destination?
Accept the shorter path.
R5
R3
R4
R2
R1
A

## Slide 14: Multiple Paths Advertised
You might not hear about both paths simultaneously.
In the forwarding table, record the best-known cost to a destination.
If your table doesn't have a path to a destination, accept any path you hear about.
R5
R3
R4
R2
R1
A
A is 3 away from me.
R5's Table |  | 
To: | Via: | Cost:
A | R3 | 4
Notes: one more problem is that you
42:05
might actually not hear about both of the paths at the same time so in the picture we had before everything was
42:10
nice R5 heard about two different paths and it got to pick the best one but that
42:16
might not always happen what if the costs come in at different times for example you your R5 and you hear about
42:23
the advertisement from R3 so R3 says I can reach a I'm 308 so what should R5 do
42:30
at this point because R5 hasn't heard the second path yet it only knows about
42:35
a single path to a so what R5 has to do for now is say well is this the best I
42:41
don't know but it's what I have right now so I'm going to go ahead and use this one for now and if I hear a better
42:47
one later I can change my mind so routers are allowed to change their mind if they hear about something better and
42:53
what that means is because routers have to be able to change their minds when they hear better routes they should also
43:00
keep track of the routes so so far our forwarding tables just said a destination and a Next Top we are now
43:07
going to add a third column that used to not be there and the third column helps us keep track of the best known cost to
43:15
the destination so before this little packet came in R5 had no idea where a
43:21
was or even that a existed but then it heard a message from R3 and R3 said I am
43:26
r three if you want to send packets to a send them through me I am cost three
43:32
away and R5 thinks well that's great if you're three away I must be four away so
43:39
I will write down that I can pass packets to R3 and they will reach a and
43:44
I'll also leave a note to myself that this best known path has cost four and
43:50
maybe I'll get a better one later who knows but for now at least I have a path to a I don't know if it's the best one
43:56
maybe maybe better ones will come along maybe no other paths will come along but that's what I have right now and later

## Slide 15: Multiple Paths Advertised
You might not hear about both paths simultaneously.
In the forwarding table, record the best-known cost to a destination.
If your table doesn't have a path to a destination, accept any path you hear about.
If you hear about a better path later, update the table (next-hop and cost).
R5
R3
R4
R2
R1
A
R5's Table |  | 
To: | Via: | Cost:
A | R3 R4 | 4 3
A is 2 away from me.
I like this new path better. I'll abandon the old one.
Notes: 44:03
you might hear a different path so now later down the line R4 sends a message to R5 and says I'm R4 I can reach a and
44:12
if you send it to me I am two away from a so R5 now thinks and realizes actually
44:17
you know what the old path that I had which was cost four is not the best one
44:22
this one is better R4 is 2 away so I must be three away so so actually this
44:27
one has cost three that's better than four three is better than four so what
44:32
R5 can now do is R5 can change its mind it says actually I don't need that path
44:38
via R3 anymore with cost 4 I really want the path via R4 with cost three that's
44:45
better so R5 says I like the new one better and it's okay to change your mind and abandon old ones so this is what you
44:52
have to do because of the fact that there are multiple paths and they might not all be revealed to you at the same
44:58
time

## Slide 16: The Distance-Vector Algorithm So Far
For each destination:
If you hear about a path to that destination, update table if:
  The destination isn't in the table.
  The advertised cost is better than best-known cost.
Then, tell all your neighbors.
Notes: we've actually already
45:55
started to build our algorithm so we'll piece it together and this slide will start from very empty to very full as we
46:01
fill in all the rules so these rules are repeated once per destination that's why it says for each destination we just did
46:08
it for a

## Slide 17: Unequal Costs
Not all link costs are 1.
When a neighbor advertises a path, the cost via that path is the sum of:
  Link cost from you to the neighbor.
  Cost from neighbor to destination (as advertised by neighbor).
R3
R1
R2
1
10
A is 5 away from me.
R3's Table |  | 
To: | Via: | Cost:
A | R1 | 1+5 = 6
Notes: 47:57
not all link costs are one so so far we were just kind of being lazy and saying all the links were one so if someone
48:02
says I am five away from a then you must be six away because your buddy was five
48:08
away you must be six away that's true of all the link costs are one but if the link costs are not all one you have to
48:15
do a little bit of math

## Slide 18: Unequal Costs
Not all link costs are 1.
When a neighbor advertises a path, the cost via that path is the sum of:
  Link cost from you to the neighbor.
  Cost from neighbor to destination (as advertised by neighbor).
R3
R1
R2
1
10
R3's Table |  | 
To: | Via: | Cost:
A | R1 | 1+5 = 6
A is 3 away from me.
This path actually costs 10+3=13. I'll keep using the cost 6 path and reject this.

## Slide 19: The Distance-Vector Algorithm So Far
For each destination:
If you hear about a path to that destination, update table if:
  The destination isn't in the table.
  Advertised cost + link cost to neighbor < best-known cost. (#1)
Then, tell all your neighbors.
Notes: 50:27
okay so to take that rule that we just talked about and write it out that summation looks like this it's the
50:33
advertised cost the cost that you received from your buddy plus the link cost to the neighbor that's what we just
Does rule one look familiar from other classes or algorithms that you’ve encountered? Can you think of any?

## Slide 20: Distributed Bellman-Ford Algorithm
Careful viewers might have noticed this operation looks familiar.
"If cost to neighbor + cost from neighbor to destination < best-known cost, accept update."
This is the relaxation operation in Dijkstra's shortest path algorithm!
Bellman-Ford is another relaxation-based shortest path algorithm.
Relax every edge repeatedly until we get shortest paths.
Unlike Dijkstra's, does not require relaxing the edges in any specific order.
Distance-vector algorithms are a distributed, asynchronous version of Bellman-Ford.
Distributed: Each router relaxes its own links. No global mastermind.
Asynchronous: Nobody is syncing when the routers do relaxations.
Notes: this thing should hopefully look very
51:34
familiar if you've taken a data structures class because this is exactly what you do to run a shortest paths
51:40
algorithm like dyra algorithm do people know Dyer's algorithm do they remember it kind of sort of okay I saw my hands
51:48
go up that's good so this is the operation in dyra algorithm that actually makes it work if you really
51:54
remember your stuff you might remember it's called relaxation although I don't really what it's called but that's the
51:59
term that people use and basically to run dyra algorithm to get the shortest paths in a graph you just do this
52:06
operation over and over again so we could actually build a distance Vector
52:13
protocol based on dyis algorithm but I'm actually going to do it based on Bellman Ford which is another shortest pass
52:20
algorithm that does the same relaxation and the reason why I use one over the other will become more clear as we keep
52:26
going but if you remember either of these algorithms which you don't have to it's
52:31
okay if you don't remember exactly how they work Dyer's algorithm relaxes things in a very specific order
52:37
to relax all the edges radiating outwards from The Source in order to get the shortest paths whereas Bellman Ford
52:43
if you've ever seen it you can relax the edges in any order that you want as long as you relax everybody enough times you
52:50
get the shortest path so the reason why I want to use Bellman Ford here instead of dstress is that b for doesn't impose
52:57
any order in which I visit all the edges I can relax all the edges in any order that I feel like whereas Dyas actually
53:04
does impose an order but both of them are based on this relaxation operation

## Slide 21: Distributed Bellman-Ford Algorithm
The centralized Bellman-Ford algorithm for a single destination:
def bellman_ford(dst, routers, links):
distance = {}; nexthop = {}
for r in routers: distance[r] = INFINITY nexthop[r] = None distance[dst] = 0 for _ in range(len(routers)-1): for (r1, r2, linkcost) in links:
if distance[r1] + linkcost < distance[r2]: distance[r2] = distance[r1] + linkcost nexthop[r2] = r1
return distance, nexthop
Everyone starts infinity away from the destination, except for the destination itself (0 away).
The relaxation operation.
Loop through nodes and relaxes repeatedly.
In distance-vector, each router relaxes in parallel, with both directions as links between routers.
Notes: Here is the centralized bellman-ford algorithm in pseudo code. Let’s step through each component and then we’ll talk about how it’s distributed.
In the distributed version have to take out this for loop. Routers can’t get in line or have a guarantee all will do this in order.
ow the difference with our version is that our version is distributed so we
58:35
don't have a list of all the routers we don't have a list of all the links no one is telling us that stuff so instead
58:42
we're still going to do the same thing but we're going to do it in a distributed way so this blue section it
58:47
still exists but instead of initializing these dictionaries the way they did in their centralized version we'll just
58:53
have every router initialize their forwarding tables to for example empty

## Slide 22: Bellman-Ford Demo
Distance-Vector Correctness
Algorithm Sketch
Rule 1: Bellman-Ford Updates
Bellman-Ford Demo
Rule 2: Updates From Next-Hop
Rule 3: Resending
Rule 4: Expiring
Distance-Vector Enhancements
Rule 5: Poison Expired Routes
Rule 6A: Split Horizon
Rule 6B: Poison Reverse
Rule 7: Count To Infinity
Eventful Updates
Lecture 5, CS 168, Spring 2026

## Slide 23: The Distance-Vector Algorithm So Far
For each destination:
If you hear an advertisement, update table if:
  The destination isn't in the table.
  Advertised cost + link cost to neighbor < best-known cost. (#1)
Then, advertise to all your neighbors.
Terminology note:
Sending "I'm R1, and I can reach A with cost 5" is called announcing or advertising a route.

## Slide 24: Bellman-Ford Demo
R1
A
R2
R3
R1's Table |  | 
To: | Via: | Cost:
R2's Table |  | 
To: | Via: | Cost:
R3's Table |  | 
To: | Via: | Cost:

## Slide 25: Bellman-Ford Demo
R1
A
R2
R3
R1's Table |  | 
To: | Via: | Cost:
A | Direct | 1
R2's Table |  | 
To: | Via: | Cost:
R3's Table |  | 
To: | Via: | Cost:
Static routing: Someone hard-codes R1's table to say it can reach A.

## Slide 26: Bellman-Ford Demo
R1
A
R2
R3
R1's Table |  | 
To: | Via: | Cost:
A | Direct | 1
R2's Table |  | 
To: | Via: | Cost:
R3's Table |  | 
To: | Via: | Cost:
I found a way to reach A!
Time to tell all my neighbors.

## Slide 27: Bellman-Ford Demo
R1
A
R2
R3
R1's Table |  | 
To: | Via: | Cost:
A | Direct | 1
R2's Table |  | 
To: | Via: | Cost:
R3's Table |  | 
To: | Via: | Cost:
I'm R1, and A is 1 away from me.
New advertisement!
I don't have a way to reach A yet, so I'll accept.
R2's Table |  | 
To: | Via: | Cost:
A | R1 | 1+1=2
1 (link cost to R1), plus 1 (advertised cost).

## Slide 28: Bellman-Ford Demo
R1
A
R2
R3
R1's Table |  | 
To: | Via: | Cost:
A | Direct | 1
R3's Table |  | 
To: | Via: | Cost:
Time to tell everyone about my shiny new path to A.
R2's Table |  | 
To: | Via: | Cost:
A | R1 | 2

## Slide 29: Bellman-Ford Demo
R1
A
R2
R3
R1's Table |  | 
To: | Via: | Cost:
A | Direct | 1
R3's Table |  | 
To: | Via: | Cost:
R2's Table |  | 
To: | Via: | Cost:
A | R1 | 2
I'm R2, and A is 2 away from me.
I'm R2, and A is 2 away from me.
Notice: R2's announcement doesn't include the next-hop. Nobody else cares how R2 reaches A, just that R2 can reach A.

## Slide 30: Bellman-Ford Demo
R1
A
R2
R3
R1's Table |  | 
To: | Via: | Cost:
A | Direct | 1
R3's Table |  | 
To: | Via: | Cost:
R2's Table |  | 
To: | Via: | Cost:
A | R1 | 2
I'm R2, and A is 2 away from me.
I'm R2, and A is 2 away from me.
New advertisement?!
This new path costs 1+2=3.
I already have a cost 1 path.
No thanks.

## Slide 31: Bellman-Ford Demo
R1
A
R2
R3
R1's Table |  | 
To: | Via: | Cost:
A | Direct | 1
R3's Table |  | 
To: | Via: | Cost:
R2's Table |  | 
To: | Via: | Cost:
A | R1 | 2
I'm R2, and A is 2 away from me.
New advertisement?!?
I don't have a path to A yet, so I'll accept.
I'm R2, and A is 2 away from me.
R3's Table |  | 
To: | Via: | Cost:
A | R2 | 1+2=3
1 (link cost to R2), plus 1 (advertised cost).

## Slide 32: Bellman-Ford Demo
R1
A
R2
R3
R1's Table |  | 
To: | Via: | Cost:
A | Direct | 1
R2's Table |  | 
To: | Via: | Cost:
A | R1 | 2
Time to advertise my exciting new path to A.
R3's Table |  | 
To: | Via: | Cost:
A | R2 | 3

## Slide 33: Bellman-Ford Demo
R1
A
R2
R3
R1's Table |  | 
To: | Via: | Cost:
A | Direct | 1
R2's Table |  | 
To: | Via: | Cost:
A | R1 | 2
R3's Table |  | 
To: | Via: | Cost:
A | R2 | 3
I'm R3, and A is 3 away from me.
New advertisement?!??!?!!!?
This new path costs 1+3=4.
I already have a cost 2 path.
No thanks.

## Slide 34: Bellman-Ford Demo
R1
A
R2
R3
R1's Table |  | 
To: | Via: | Cost:
A | Direct | 1
R2's Table |  | 
To: | Via: | Cost:
A | R1 | 2
R3's Table |  | 
To: | Via: | Cost:
A | R2 | 3
We did it! Everybody has a way to reach A now.
A this way
A this way
A this way

## Slide 35: Rule 2: Updates from Next-Hop
Distance-Vector Correctness
Algorithm Sketch
Rule 1: Bellman-Ford Updates
Bellman-Ford Demo
Rule 2: Updates From Next-Hop
Rule 3: Resending
Rule 4: Expiring
Distance-Vector Enhancements
Rule 5: Poison Expired Routes
Rule 6A: Split Horizon
Rule 6B: Poison Reverse
Rule 7: Count To Infinity
Eventful Updates
Lecture 5, CS 168, Spring 2026

## Slide 36: Updates From the Current Next-Hop
Recall our routing challenges: Topology can change.
So far: We update if we get a better path (or if we didn't have a path before).
Fix: If our current next hop sends us an announcement, accept it, even if the path is worse.
This lets the next-hop notify us if the topology changed.
R3
R1
R2
R3's Table |  | 
To: | Via: | Cost:
R3's Table |  | 
To: | Via: | Cost:
A | R2 | 1+3 = 4
I'm R2, and A is 3 away from me.
A wasn't in my table. Accept!
Notes: 1:12:28
actually the topology might have changed maybe like a link went down or an operator changed the cost of one of the
1:12:35
links so I know I said it's three earlier but I've actually changed my mind the graph itself has changed so I
1:12:42
have changed my mind and a should really be eight away so when you see a message
1:12:47
like this you're tempted to see it and say oh was a and nine that's worse than four reject but actually R2 might be
1:12:54
trying to tell you something it's trying to tell you hey the path has actually
1:12:59
changed because the network topology itself changed so you should really
1:13:04
listen to me because I'm trying to tell you new information so we need to change our rule to not just reject all things
1:13:11
that are worse but we need to accept in a case like this so R3 really should say
1:13:19
well I currently am going via R2 but R2 has just come along and told me that
1:13:24
they changed their mind so this really shouldn't say four anymore what should it say this should
1:13:29
really say nine so I'm still forwarding via R2 to a but the new cost is nine

## Slide 37: Updates From the Current Next-Hop
Recall our routing challenges: Topology can change.
So far: We update if we get a better path (or if we didn't have a path before).
Fix: If our current next hop sends us an announcement, accept it, even if the path is worse.
This lets the next-hop notify us if the topology changed.
R3
R1
R2
R3's Table |  | 
To: | Via: | Cost:
A | R2 | 4
I'm R1, and A is 8 away from me.
1+8=9 is worse than 4.
Reject!

## Slide 38: Updates From the Current Next-Hop
Recall our routing challenges: Topology can change.
So far: We update if we get a better path (or if we didn't have a path before).
Fix: If our current next hop sends us an announcement, accept it, even if the path is worse.
This lets the next-hop notify us if the topology changed.
R3
R1
R2
I'm R2, and A is 8 away from me.
R2 is the next-hop. Accept!
R3's Table |  | 
To: | Via: | Cost:
A | R2 | 4
R3's Table |  | 
To: | Via: | Cost:
A | R2 | 1+8=9
Hi, it's R2 again. I know I said A is 3 away from me earlier, but that's changed. Now A is 8 away.
What R2 is really saying:

## Slide 39: Convergence
If the network never changes:
After running this protocol for some time, it will converge.
Everyone's forwarding table has the least-cost next hop.
All future announcements will be rejected.
If a change happens (e.g. a link goes down):
Some new announcements are sent.
Some forwarding tables are updated.
Eventually, we converge again to the new routing state.
The network topology is constantly changing, so routers run the protocol indefinitely.
Steady-state occurs when the network has converged.
In steady-state, everything stays the same until the next topology change.

## Slide 40: The Distance-Vector Algorithm So Far
For each destination:
If you hear an advertisement, update table if:
  The destination isn't in the table.
  Advertised cost + link cost to neighbor < best-known cost. (#1)
  The advertisement is from current next-hop. (#2)
Then, advertise to all your neighbors.

## Slide 41: Rule 3: Resending
Distance-Vector Correctness
Algorithm Sketch
Rule 1: Bellman-Ford Updates
Bellman-Ford Demo
Rule 2: Updates From Next-Hop
Rule 3: Resending
Rule 4: Expiring
Distance-Vector Enhancements
Rule 5: Poison Expired Routes
Rule 6A: Split Horizon
Rule 6B: Poison Reverse
Rule 7: Count To Infinity
Eventful Updates
Lecture 5, CS 168, Spring 2026

## Slide 42: Ensuring Reliability
Recall our routing challenges: Packets can get dropped.
Solution: Resend advertisements every X seconds.
X is the "advertisement interval."
This should work eventually, assuming the link is functional (>0% delivery rate).
R1
A
R2
R3
R1's Table |  | 
To: | Via: | Cost:
A | Direct | 1
R2's Table |  | 
To: | Via: | Cost:
R3's Table |  | 
To: | Via: | Cost:
I'm R1, and A is 1 away from me.
Huh? Did someone say something?
Dropped!
Notes: let's take care of another one another problem with the routing protocol and routing protocols
5:22
in general is that they are running on layer three which is best effort and best effort means that packets can get
5:29
dropped so it could be the case that R1 has this new shiny path to a it's all great but
5:35
when it tries to tell R2 back it gets dropped R2 doesn't hear anything that's a problem R2 is not going to learn the
5:43
path to a that's a problem and we're going to solve it with probably the simplest dumbest solution to best effort
5:51
and that is to resend the advertisements every so often so instead of just
5:57
sending this advertisement once and saying saying I'm R1 I can reach a with
6:02
cost one you're going to send that exact same advertisement once every few seconds and
6:09
the number of seconds is the advertisement interval I think in practice it's like every 10 seconds or
6:14
every one second order of seconds as opposed to milliseconds or something that' be too fast but roughly the order
6:21
of a couple seconds that's called the advertisement interval and you send it over and over and over again and even if
6:28
it doesn't work the first time the second time or the third time it should work eventually assuming that something
6:34
gets through this packet or this link this should work eventually after some time if every single packet gets dropped
6:42
you might ask if that link even counts because it's dropping everything there a link that drops everything even count as
6:47
a link kind of philosophical not that important but basically that's our
6:52
solution to ensuring reliability is just sending the same thing over and over and over again
7:02
okay so back to our favorite list of rule

## Slide 43: The Distance-Vector Algorithm So Far
For each destination:
If you hear an advertisement, update table if:
  The destination isn't in the table.
  Advertised cost + link cost to neighbor < best-known cost. (#1)
  The advertisement is from current next-hop. (#2)
Advertise to all your neighbors when the table updates, and periodically. (#3)

## Slide 44: Rule 4: Expiring
Distance-Vector Correctness
Algorithm Sketch
Rule 1: Bellman-Ford Updates
Bellman-Ford Demo
Rule 2: Updates From Next-Hop
Rule 3: Resending
Rule 4: Expiring
Distance-Vector Enhancements
Rule 5: Poison Expired Routes
Rule 6A: Split Horizon
Rule 6B: Poison Reverse
Rule 7: Count To Infinity
Eventful Updates
Lecture 5, CS 168, Spring 2026

## Slide 45: Handling Failures
Recall our routing challenges: Links and routers can fail.
Solution: Each route has a finite time to live (TTL).
Periodic advertisements help us confirm that a route still exists.
  When we get an advertisement, reset ("recharge") the TTL.
If a link goes down, we stop getting periodic updates, and the TTL will expire.
  If the TTL expires, delete the entry from the table.
R3
R2
Didn't have a path to A. Accept!
R3's Table |  |  | 
To: | Via: | Cost: | TTL:
I'm R2, and A is 5 away from me.
R3's Table |  |  | 
To: | Via: | Cost: | TTL:
A | R2 | 6 | 11
t = 0
Need another confirmation of this route in the next 11 seconds.
A

## Slide 46: Handling Failures
Recall our routing challenges: Links and routers can fail.
Solution: Each route has a finite time to live (TTL).
Periodic advertisements help us confirm that a route still exists.
  When we get an advertisement, reset ("recharge") the TTL.
If a link goes down, we stop getting periodic updates, and the TTL will expire.
  If the TTL expires, delete the entry from the table.
R3's Table |  |  | 
To: | Via: | Cost: | TTL:
A | R2 | 6 | 10
t = 1
t = 2
9
t = 3
8
t = 4
7
R3
R2
A

## Slide 47: Handling Failures
Recall our routing challenges: Links and routers can fail.
Solution: Each route has a finite time to live (TTL).
Periodic advertisements help us confirm that a route still exists.
  When we get an advertisement, reset ("recharge") the TTL.
If a link goes down, we stop getting periodic updates, and the TTL will expire.
  If the TTL expires, delete the entry from the table.
R3's Table |  |  | 
To: | Via: | Cost: | TTL:
A | R2 | 6 | 11
t = 5
We got a confirmation! Reset TTL back to 11.
I'm still R2, and A is still 5 away from me.
R3
R2
A

## Slide 48: Handling Failures
Recall our routing challenges: Links and routers can fail.
Solution: Each route has a finite time to live (TTL).
Periodic advertisements help us confirm that a route still exists.
  When we get an advertisement, reset ("recharge") the TTL.
If a link goes down, we stop getting periodic updates, and the TTL will expire.
  If the TTL expires, delete the entry from the table.
R3's Table |  |  | 
To: | Via: | Cost: | TTL:
A | R2 | 6 | 10
t = 6
9
t = 7
8
t = 8
7
t = 9
Link goes down!
6
t = 10
5
t = 11
4
t = 12
3
t = 13
2
t = 14
1
t = 15
R3
R2
A

## Slide 49: Handling Failures
Recall our routing challenges: Links and routers can fail.
Solution: Each route has a finite time to live (TTL).
Periodic advertisements help us confirm that a route still exists.
  When we get an advertisement, reset ("recharge") the TTL.
If a link goes down, we stop getting periodic updates, and the TTL will expire.
  If the TTL expires, delete the entry from the table.
R3's Table |  |  | 
To: | Via: | Cost: | TTL:
A | R2 | 6 | 0
t = 16
Timeout! Delete expired entry.
Link goes down!
R3
R2
A

## Slide 50: Timers
Routers maintain multiple timers:
Advertisement interval: How long before we advertise routes to neighbors.
  Usually one timer for all entries in the table.
TTL: How long before we expire a route.
  Each table entry has its own TTL.

## Slide 51: The Distance-Vector Algorithm
For each destination:
If you hear an advertisement, update table and reset TTL if:
  The destination isn't in the table.
  Advertised cost + link cost to neighbor < best-known cost. (#1)
  The advertisement is from current next-hop. (#2)
Advertise to all your neighbors when the table updates, and periodically. (#3)
If a table entry expires, delete it. (#4)
Notes: Before we keep going. Can anyone think of any optimization ideas?? For each destination:
If you hear an advertisement, update table and reset TTL if:
  The destination isn't in the table.
  Advertised cost + link cost to neighbor < best-known cost. (#1)
  The advertisement is from current next-hop. (#2) Includes poison advertisements. (#5)
Advertise to all your neighbors when the table updates, and periodically. (#3)
  But don't advertise back to the next-hop. (#6A)
  ...Or, advertise poison back to the next-hop. (#6B)
  Any cost ≥ 16 is advertised as ∞. (#7)
If a table entry expires, make the entry poison and advertise it. (#3, #5)

## Slide 52: Summary: Distance-Vector Rules
1. Bellman-Ford Updates: Accept if advertised cost + link cost to neighbor < best-known cost.
2. Updates From Next-Hop: Accept if advertisement is from next hop.
3. Resending: Advertise periodically.
4. Expiring: Expire an entry if TTL runs out.