## Slide 1: Bandwidth and Propagation Delay Exercises ANS
Links
Bandwidth and Propagation Delay
Pipe Diagrams
Overloaded Links
Brief Preview of the Semester
Lecture 3, Spring 2026
Notes: so here's the outline we're going
38:16
to start by talking about links in a lot of detail think about how you measure the performance of links what makes a
38:21
link good what makes a link bad what are the trade-offs we'll talk about what happens if links get overloaded and then
38:27
the very end now that we finished all of the introduction I can actually give you a preview of all the topics you're going
38:33
to see in a lot more detail so these three sets of lectures have really been about giving you a highlevel 10,000 foot
38:39
picture of what you're going to see this semester and then at the very end I'll show you the exact places where we'll be
38:45
really diving in and talking about things in lots more detail but before we get there let's not get ahead of
38:50
ourselves let's start with talking about links and how to measure their performanc

## Slide 2: Packet delay: four sources
dq: queueing delay
time waiting at output link for transmission
depends on congestion level of router
propagation
queueing
dnodal = dqueue + dtrans + dprop
A
B
transmission
dtx: transmission delay:
L: packet length (bits)
R: link transmission rate (bps)
dtrans = L/R
dprop: propagation delay:
d: length of physical link
s: propagation speed (~2x108 m/sec)
dprop = d/s
IMPORTANT
The nodal processing delay (check bit errors, determine output link) is typically very small and can be ignored
Notes: dproc: nodal processing
check bit errors
determine output linknodal processing
typically < microsecs

## Slide 3: Q1 End-­to­‐end delay
Consider the network shown in the figure, with three links, each with a transmission rate of 1 Mbps, and a propagation delay of 1 msec per link. Assume the length of a packet is 1000 bits.
What is the end-end delay of a packet from when it first begins transmission on link 1, until is it received in full by the server at the end of link 3. Assume that queueing delays are zero.
Notes: Each link has transmission delay 1000 bits/1 Mbps = 1ms. So each link has total delay of transmission + propagation = 1+1=2 ms.
For the three links, the total delay = 2 + 2 + 2 = 6 ms. `

## Slide 4: Q1 End-­to­‐end delay ANS
Packet length bits, link rate Mbps → transmission delay per link s = 1 ms.
Propagation delay per link = 1 ms.
Each link contributes ms.
Three links → total ms = 6 ms.

## Slide 5: Q2 End-­to­‐end delay
Consider the scenario shown in Figure 1: a server is connected to a router by a 100Mbps link with a 50ms propagation delay. This router is connected to two other routers, each over a 50Mbps link with a 200ms propagation delay. A 1Gbps link connects each host to each of these routers with 0 propagation delay. All packets in the network have size of 20,000 bits.
What is the end-­to­‐end delay (in ms) from when a packet is transmitted by the server to when it is received by the client? Assume there’s no queuing delay at the routers.

## Slide 6: Q1 End-­to­‐end delay ANS
Transmission delays:
100 Mbps link:s = 200 μs
50 Mbps link:s = 400 μs
1 Gbps link:s = 20 μs
Total transmission delay: μs = 0.62 ms
Propagation delays:
Server → router: 50 ms
Router → router: 200 ms
Router → client: 0 ms
Total propagation delay:ms
End-to-end delay
Notes: ANS: If all packets are 20,000 bits long it takes 200 us to send the packet over the 100Mbps link, 400 usec to send over the 50Mbps link, and 20 us to send over the 1Gbps link. Sum of the three-link transmission is 620 us = 0.62 ms. Thus, the total end-to-end delay is 250 + 0.62 = 250.62 ms.
(Detailed calculations shown on the right.)

## Slide 7: Q3 End-­to­‐end delay
Consider a 100 Mbps link between an earth station (sender) and a satellite (receiver) at an altitude of 2100 km. The signal propagates at a speed of m/s. Calculate the time taken (in ms) for the receiver to receive a packet of 1000 bytes transmitted by the sender. (There is no router so there is no queuing delay.)

## Slide 8: Q3 End-­to­‐end delay ANS
1. Transmission delay.
Packet size:bytes bits
Link rate:Mbps bits/s
2. Propagation delay
Distance:km m
Propagation speed:m/s
3. Total delay

## Slide 9: Q4 End-­to­‐end delay
Consider two computers X and Y connected via a single link of bandwidth 512 Gbps. Suppose that both hosts are separated by distance M meters, and the propagation delay along the link is meters/sec. Computer X has to send a packet of size 1 Kbyte to computer Y. What will be the distance M such that the propagation delay is equal to the transmission delay?

## Slide 10: Q4 End-­to­‐end delay ANS
Step 1: Transmission delay
(1 Kbyte = 1024 bytes = 1024×8 = 8192 bits. Notice it is NOT 1000 bytes.)\
Step 2: Propagation delay
Step 3: Set them equal
meters

## Slide 11: Q5 Transmission delay
1. Calculate transmission delay for message size bits, network bandwidth bits/sec
ANS:
2. Calculate transmission delay for message size , network bandwidth
ANS:
Notes: Computer Networks 14 | Delay in Computer Network | CS & IT | GATE Crash Course
https://www.youtube.com/watch?v=vXyNFzq7Ixc&list=PL3eEXnCBViH-hlNCNwdfV7VrEcTquANGa&index=15

## Slide 12: Q5 Transmission delay ANS
1. Calculate transmission delay for message size bits, network bandwidth bits/sec
ANS:
2. Calculate transmission delay for message size , network bandwidth
ANS:
Notes: Computer Networks 14 | Delay in Computer Network | CS & IT | GATE Crash Course
https://www.youtube.com/watch?v=vXyNFzq7Ixc&list=PL3eEXnCBViH-hlNCNwdfV7VrEcTquANGa&index=15