## Slide 1
Slides credit: CS168@UC Berkeley
Wireless Links
Lecture 24 (Wireless 1)
Notes: Others: Andrea Goldsmith, Neal Patwari, Kyle Jamieson
Slides template credit: Josh Hug, Lisa Yan

## Slide 2: Why is Wireless Different?
Why is Wireless Different?
Shared Medium
Attenuation
Changing Environments
Collision Detection
Lecture 24, Spring 2026

## Slide 3: Wireless Signals
Wireless signals are waves that propagate in all directions.
Analogy: Ripples in a pond.
Waves interact with each other, and with the environment.
Differences mostly affect Layer 1 (Physical) and Layer 2 (Link).
Wireless is fundamentally a shared medium. (Wired is not.)
Wireless signals attenuate significantly with distance. (Wired signals do not.)
Wireless environments can change rapidly. (Wired environments do not.)
Wireless packet collisions are hard to detect. (Wired packet collisions are not.)
A
B
Notes: Wireless signals are not packets of data floating in space.

## Slide 4: Difference: Wired vs. Wireless Links
Wired links:
Point-to-point (private) by default.
Creating multi-point buses requires work.
Fairly easy to shield from external interference.
Uses electrical signals to transmit data.
Wireless links:
Broadcast (shared) by default.
Creating point-to-point private links requires work.
Fairly hard to shield from external interference.
Modulate electromagnetic fields to transmit data.
Notes: https://commons.wikimedia.org/wiki/File:600V_CV_5.5sqmm.jpg

## Slide 5: Encoding Data Over Wireless Links
Wired link: Encode bits as electrical signals.
High voltage = 1.
Low voltage = 0.
Wireless link:
Draw the bits as a wave?
Problem: Resulting wave is low-frequency, and hard to transmit.
0 0 1 1 0 0 0 0 0 1 0 1 0 1 1 1 1 0 0 0 0

## Slide 6: Encoding Data Over Wireless Links – Modulation
Modulation: Impose our data signal on top of a carrier signal.
Carrier signal: A high-frequency, constant wave that contains no information.
The combined wave is easy to transmit, and contains our data!
Amplitude Modulation (AM):
1 = Taller wave.
0 = Shorter wave.
Frequency Modulation (FM):
1 = Oscillate fast.
0 = Oscillate slow.
Original signal
+ Carrier signal
= Modulated signal
Other modulation strategies exist.

## Slide 7: Measuring Noise and Interference – SINR
Shared medium → other signals can corrupt our data!
Noise: Background, ambient signals.
Interference: Another transmitter sending signals.
SINR (Signal to Interference and Noise Ratio) lets us measure connection quality:
Ratio of power to noise+interference at the the receiver.
Higher SINR is better.
If there's more noise+interference, the signal must be stronger.
If signal is weak, can employ coding gain (error-correcting codes).

## Slide 8: Measuring Noise and Interference – SINR
SINR is dimensionless (it's a ratio).
Decibels let us measure ratios on a logarithmic scale.
Ratio is 10 times greater = increase of 10 dB.
Ratio | Ratio in dB
1 | 0 dB
10 | 10 dB
100 | 20 dB
1000 | 30 dB
10000 | 40 dB
SINR formula.
SINR (measured in dB).

## Slide 9: Measuring Noise and Interference – Noisy Channel Shannon Capacity
Shannon capacity: Theoretical limit of how much data can be sent on a noisy channel.
How much data can be sent? (bits/sec)
Bandwidth of channel (range of frequencies we can use).
Ratio of signal power to noise+interference.
Higher bandwidth = can send more data.
SINR increases = can send more data.
  Stronger signal, or less noise+interference.
Example: The plain old telephone system:
B = 3000 Hz. (Telephones understand frequencies between 300 Hz and 3300 Hz.)
SINR = 100. (20 dB signal-to-noise ratio.)
C = 3000 · log2(1 + 100) ≈ 20000 = 20 kbps.
Notes: Bandwidth here is a range of frequencies which is different from how we’ve been using it. It’s the EE bandwidth.

## Slide 10: Difference: Wireless Signals Attenuate
Why is Wireless Different?
Shared Medium
Attenuation
Changing Environments
Collision Detection
Lecture 24, Spring 2026

## Slide 11: Difference: Attenuation
Wireless signals attenuate – they get much weaker over longer distances.
Our design must account for attenuation.
Wired signals also attenuate, but effect is far smaller.
Trade-off:
Maximize performance: Accuracy, speed, range.
Minimize resource use: Power, use less of the frequency spectrum (costs money).
Trade-off: Better signal requires more resources.

## Slide 12: Measuring Attenuation – Free-Space Model
Free-space model (aka line-of-sight model):
Transmitter and receiver exist in empty space.
No obstacles, not even Earth's surface.
In this model, the inverse square law applies.
10 times as far = signal is 100 times weaker.
k times as far = signal is k2 times weaker.
Receiver power
d = distance between transmitter and receiver
Transmitter power
Intuition: Signal propagates out like a sphere.
Signal power is spread over surface of sphere. Surface area of sphere = 4πr2.
"is proportional to"
Distance
Signal Strength
Notes: https://commons.wikimedia.org/wiki/File:Inverse_square_law.svg

## Slide 13: Measuring Attenuation – Friis Equation
The Friis equation accounts for:
Gain of the transmitter and receiver antennas.
Aperture (area) of the receiver antenna. Proof omitted.
  Intuition: Larger antenna can capture more signal.
Distance between antennas (inverse-square law).
Receiver power
Transmitter power
Gains of antennas
Aperture of receiver antenna
Distance (inverse square law)
Notes: D here is distance not diameter
Longer wavelengths = larger effective aperture

## Slide 14: Measuring Attenuation – Friis Equation, Rewritten
The equation is sometimes written like this:
Or in terms of decibels (logarithmic scale):

## Slide 15: Measuring Attenuation – Link Budget
How do we know if the link will actually work?
Compute a link budget: Add all gains, subtract all losses.
Compare:
  Signal power at receiver.
  Receiver sensitivity (minimum signal the receiver can hear).
If link budget is positive: Pr > Sensitivity. Link works!
If link budget is negative: Pr < Sensitivity. Link doesn't work!
Link margin is difference between receiver signal and sensitivity.
Bigger link margin = more robust signal.

## Slide 16: Measuring Attenuation – Link Budget
Example of computing link budget:
Transmitter
Receiver
Sensitivity: –80 dBm
Transmitted Signal: +10 dBm
Cable: –0.44 dB
Cable: –2.21 dB
Cable: –0.44 dB
Cable: –2.21 dB
Antenna: +25 dB
Antenna: +25 dB
Signal travels 10km: –120 dB
Received Signal: –65.5 dBm
Link margin = 14.5 dBm > 0. Our connection works!
Note: dBm = Power relative to 1 milliwatt.
Notes: 0 dBm = 1 mW
10 dBm = 10 mW
20 dBm = 100 mW
30 dBm = 1 W
-10 dBm = 0.1 mW
-20 dBm = 0.01 mW
-65.5 = 0.0000002818 mW
Adding dB is like multiplying by a ratio, so this might seem odd but is ok :)

## Slide 17: Difference: Changing Environments
Why is Wireless Different?
Shared Medium
Attenuation
Changing Environments
Collision Detection
Lecture 24, Spring 2026

## Slide 18: Difference: Environments Change
Wireless environments change rapidly.
Devices move around.
Signals reflect and refract off physical obstacles (e.g. buildings, Earth's surface).
Distance
Signal Strength
Free-space model: Signal weakens over distance.
Distance
Signal Strength
After accounting for obstacles: Signal strength fluctuates!

## Slide 19: Path Loss is Messy
Wireless propagation is messy.
In theory: Signal propagates in all directions.
In real life: Signal strength depends on environment.
Color = strength of signal.
Notes: Credit: Neal Patwari

## Slide 20: Characteristics of Path Loss
3 characteristics affect signal strength:
Distance
Signal Strength
Free-space loss:
– Due to inverse square law. – Fluctuates very slowly.
Shadowing:
– Due to obstructions. – Fluctuates quickly.
Multipath fading:
– Due to signal colliding with itself. – Fluctuates very quickly.
Distance
Signal Strength
Distance
Signal Strength
Distance
Signal Strength
+

## Slide 21: Modeling Path Loss – Two-Ray Model
Two-ray model assumes the signal waves travel along two paths:
Line-of-sight path: Wave arrives with no obstacles.
Ground-bounce path: Wave reflects off the Earth's surface.
Assuming sender and receiver are far enough:
Two waves arrive phase-shifted at the receiver, causing destructive interference.
Signal strength ∝ 1/d4. Drops off much faster than inverse-square law!
Earth's surface
Sender tower
Receiver tower
Line-of-sight path
Ground bounce path
Time
Signal
Time
Signal
=
Signal arrives with phase offset...
...canceling each other out!

## Slide 22: Modeling Path Loss – Two-Ray Model
If sender and receiver are far enough:
Waves arrive phase-shifted at the receiver, causing destructive interference.
Signal strength ∝ 1/d4. Drops off much faster than inverse-square law!
Distance
Signal Strength
Free-space model:
– Signal strength ∝ 1/d2. – Idealized, no obstacles.
Distance
Signal Strength
Two-ray model:
– Signal strength ∝ 1/d4. – Signal bounces off ground. Causes destructive interference.

## Slide 23: Modeling Path Loss – General Ray Tracing Models
General ray tracing models account for other obstacles.
Signals reflect, scatter, and diffract.
Most signals arriving at receiver are reflections.
Run simulations in software. Requires information about environment.
Earth's surface
Sender
Receiver
Obstacle
Obstacle
Obstacle

## Slide 24: Modeling Path Loss – General Ray Tracing Models
Free-space model: Signal strength ∝ 1/d2.
Two-ray model: Signal strength ∝ 1/d4.
General ray tracing model:
Receiver power
Transmitter power
Distance
K and γ are empirically determined by the model.
Signal dominated by reflections.
Exponent γ is determined empirically. Usually between –2 and –8.

## Slide 25: Difference: Collision Detection
Why is Wireless Different?
Shared Medium
Attenuation
Changing Environments
Collision Detection
Lecture 24, Spring 2026

## Slide 26: Difference: Collision Detection
Wired collisions are easy to detect.
On a point-to-point link, collisions might not happen at all.
There's just one signal on the wire to sense.
Wireless collisions are much harder to detect.
There's a spatial aspect to collisions.
Signals can collide in one place, but not another place.
A
B
Signals collide here.
No collision here!
No collision here!

## Slide 27: Recall: Multiple Access Protocols
Recall: Many ways for devices to share a link.
Let's start with CSMA: Listen, and transmit when it's quiet.
Then we'll design some protocols for wireless networks.
CSMA/CD
CSMA
ALOHA
Tokens
Polling
Multiplexing
Taking Turns
Random Access
Multiple Access Protocols
Frequency
Time

## Slide 28: CSMA in Wireless Networks
If pairs are well-separated, no problem!
Goal: A→B and C→D.
A transmits to B.
C transmits to D at the same time.
No collisions!
Notice: Signals propagate in all directions (not just toward the destination).
Arrows are just drawn for convenience.
A
C
B
D

## Slide 29: CSMA in Wireless Networks
A is quiet now. My turn!
If pairs are in range of each other, no problem!
Goal: A→B and C→D.
A transmits to B.
C detects transmission. Must wait to transmit to D.
No collisions! A–B and C–D take turns.
A
C
B
D
I hear A transmitting!
I'll wait for A to finish.

## Slide 30: CSMA in Wireless Networks – Hidden Terminal Problem
Hidden terminal problem:
Goal: A→B and C→B.
A senses quiet, and starts transmitting.
C senses quiet, and starts transmitting.
Collision at B!
Problem: A and C are out-of-range. They can't detect each other sending.
A
C
B
All is quiet. Time to send!
All is quiet. Time to send!
???

## Slide 31: CSMA in Wireless Networks – Exposed Terminal Problem
Exposed terminal problem:
Goal: B→A and C→D.
B senses quiet, and starts transmitting.
C senses a collision and doesn't send.
Notice: We could have actually sent simultaneously.
Some areas have collision, but we don't care. No collisions at the receivers.
A
C
B
D
All is quiet. Time to send!
I hear B.
I'll be quiet.
This would have been okay! But C didn't send.

## Slide 32: MACA (Multiple Access with Collision Avoidance)
Key problem: CSMA detects collisions at the sender.
But we only care about collisions at the receiver.
Solution: Let's have the receiver announce if it detects collisions.
New protocol for shared medium: MACA (Multiple Access with Collision Avoidance).
Note: No carrier sense.

## Slide 33: MACA (Multiple Access with Collision Avoidance)
To communicate over MACA:
Sender transmits Request to Send (RTS) with length of data.
Receiver transmits a Clear to Send (CTS) with length of data.
  This tells sender that it's safe to send. No collisions at receiver.
  This tells everyone in receiver's range to be quiet.
A
B
RTS: "I want to send 1 MB."
CTS: "If you hear this, shut up. I need to receive 1 MB."
A sends 1 MB.

## Slide 34: MACA (Multiple Access with Collision Avoidance) – Solving Hidden Terminal Problem
MACA solves the hidden terminal problem.
Goal: A→B, C→B.
B now tells everyone in its range to be quiet, using the CTS.
C won't send anymore. Collision avoided!
A
C
B
RTS: "I want to send 1 MB."
CTS: "If you hear this, shut up. I need to receive 1 MB."
B told me to be quiet. I won't send.
A sends 1 MB.
C would have sent, but MACA saved the day!

## Slide 35: MACA (Multiple Access with Collision Avoidance) – Rules
If you hear a CTS, be quiet until the data is sent.
CTS contains length of data.
You can use data length to estimate how long you need to wait.
If you hear an RTS, be quiet for one time slot.
Give the receiver time to send the CTS.
  If you don't be quiet, you might clobber out the CTS.
After waiting:
  If you hear the CTS: You're in receiver range. Be quiet.
  If you don't hear the CTS: You're not in receiver range. You can send again.

## Slide 36: MACA (Multiple Access with Collision Avoidance) – Solving Exposed Terminal Problem
MACA solves the exposed terminal problem, under certain assumptions.
Goal: B→A and C→D.
C hears the RTS and defers for one time slot.
C doesn't hear the CTS, so it's out-of-range of the other receiver, and can send.
A
C
B
D
I hear an RTS. I'll be quiet for 1 time slot to avoid clobbering the CTS.
RTS: "I want to send 1 MB."
CTS: "If you hear this, shut up. I'm receiving 1 MB."
B sends 1 MB.
C quiet at this time.
I didn't hear the CTS. I'm not in receiver range. I can send data!
C can send here too! (After its own RTS/CTS.)

## Slide 37: MACA (Multiple Access with Collision Avoidance) – Solving Exposed Terminal Problem
MACA solves the exposed terminal problem, under one assumption.
Assumes that C can hear the CTS from D over B's data.
Key problem: MACA requires the sender to listen (for the CTS).
  Contrast with CSMA: Sender just sends.
A
C
B
D
RTS: "I want to send 1 MB."
CTS: "If you hear this, shut up. I'm receiving 1 MB."
B sends 1 MB.
C quiet at this time.
RTS: "I want to send 1 MB."
CTS from D.
Did I hear CTS from D, or data from B?

## Slide 38: MACA (Multiple Access with Collision Avoidance) – Collisions
If we send RTS, but don't hear CTS, that means there was a collision!
Apply exponential backoff and wait up to twice as long before sending another RTS.
Each device maintains a CW (Contention Window) value.
Pick a random number in [0, CW]. Wait that long before re-sending RTS.
Rules for adjusting CW:
Minimum value: CW = 2.
Maximum value: CW = 64.
On successful RTS/CTS: Set CW ← 2.
On failed RTS/CTS: Set CW ← 2 × CW, clamped at 64.

## Slide 39: Chapter 7 outline
Introduction
Wireless
Wireless links and network characteristics
CDMA: code division multiple access
WiFi: 802.11 wireless LANs
Bluetooth

## Slide 40: Review: FDMA and TDMA
User 1
User 2
User n
…
Time
Frequency
First generation (1G) systems use Frequency Division Multiple Access (FDMA)
User 1
User 2
User n
…
Time
Frequency
Most of second generation (2G) systems use Time Division Multiple Access (TDMA)

## Slide 41: Code Division Multiple Access (CDMA)
User 1
Time
Frequency
Users share bandwidth by using code sequences that are orthogonal to each other
Some 2G and most 3G systems use CDMA
User 2
User n
Code
.
.
.
IMPORTANT

## Slide 42: Code Division Multiple Access (CDMA)
unique “code” assigned to each user; i.e., code set partitioning
  all users share same frequency, but each user has own chipping sequence (i.e., code) to encode data
  allows multiple users to “coexist” and transmit simultaneously with minimal interference (if codes are “orthogonal”)
  analogy: people speaking different languages in the same roo do not interfere with each other
encoding: scalar-vector product: (original data) (chipping sequence)
  d (x1, x2, … , xn) = (d*x1, d*x2, …, d*xn), where d = +1 or -1.
decoding: vector-vector inner-product: (encoded data) (chipping sequence)
  Defined as sum of elementwise product:
  (x1, x2, … , xn) (y1, y2, … , yn) = (x1*y1+x2*y2+…+xn*yn)
IMPORTANT

## Slide 43: Vector-Vector Inner-Product, Orthogonal Vector
For a vector x = (x1, x2, … , xn), the inner product (or dot product) with itself is given by: x x = (x1)2+(x2)2+…+(xn)2.
  This scalar value is also known as the squared norm of the vector. It is always non-negative and equals zero if and only if the vector itself is the zero vector.
  If each element xi= +1 or -1, then x x = 1+1+…+1 = n, the vector dimension.
A vector y = (y1, y2, … , yn) is the orthogonal vector of vector x=(x1, x2, … , xn) if their inner product is zero: x = (x1, x2, … , xn) (y1, y2, … , yn) = (x1*y1+x2*y2+…+xn*yn)=0
Notes: The square root of this value gives the Euclidean norm (or length) of the vector:∥v∥=v⋅v∥v∥=v⋅v​

## Slide 44: Direct-Sequence Spread Spectrum CDMA
Chipping sequence (Code): (+1,+1,+1,-1,+1,-1,-1,-1)
The 8-bit sequence 1*(+1,+1,+1,-1,+1,-1,-1,-1) encodes data bit 1 (corresponding to application bit 1).
The 8-bit sequence (-1)*(+1,+1,+1,-1,+1,-1,-1,-1) = (-1,-1,-1,1,-1,1,1,1) encodes data bit -1 (corresponding to application bit 0).
Spreading factor = Code length/data bit = 8
  10-100 commercial (Min 10 by FCC), 10,000 for military
Two codes are orthogonal to each other, if their inner product equals 0.
+1
+1
+1
+1
-1
-1
-1
IMPORTANT
Notes: Signal bandwidth > 10 × data bandwidth
Code sequence synchronization
Zi,m= di.cm
-1*(1,1,1,-1,1,-1,-1,-1) = (-1,-1,-1,1,-1,1,1,1)
1*(1,1,1,-1,1,-1,-1,-1) = (1,1,1,-1,1,-1,-1,-1)
Correlation between codes  Interference  Orthogonal

## Slide 45: CDMA encode/decode
slot 1
slot 0
d1 = -1
1
1
1
1
1
-
1
-
1
-
1
-
Zi,m= di.cm
d0 = 1
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
slot 0
channel
output
slot 1
channel
output
channel output Zi,m
sender
code
data
bits
slot 1
slot 0
d1 = -1
d0 = 1
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
slot 0
channel
output
slot 1
channel
output
receiver
code
received
input
di = S Zi,m.cm
m=1
M
M
Encoded data in slot 1:
-1*(+1,+1,+1,-1,+1,-1,-1,-1)
= (-1,-1,-1,+1,-1,+1,+1,+1)
Decoded data in slot 1:
= (1/8)*(-1,-1,-1,1,-1,+1,+1,+1) ⋅ (+1,+1,+1,-1,+1,-1,-1,-1)
= -1
IMPORTANT

## Slide 46: CDMA encode/decode
Sender 1 Code : (+1,+1,+1,-1,+1,-1,-1,-1)
Encoded data in slot 1:
  -1*(+1,+1,+1,-1,+1,-1,-1,-1)
  = (-1,-1,-1,1,-1,+1,+1,+1)
Decoded data in slot 1 is normalized (divided by code length ) inner product of the encoded with Sender 1 Code:
  = (1/8)*(-1,-1,-1,+1,-1,+1,+1,+1) (+1,+1,+1,-1,+1,-1,-1,-1)
  = (1/8)*((-1)*1+(-1)*1+(-1)*1+1*(-1) +(-1)*1+1*(-1)+1*(-1)+1*(-1))
  = (1/8)*(-8)
  = -1
IMPORTANT

## Slide 47: CDMA: two-sender interference
using same code as sender 1, receiver recovers sender 1’s original data from summed channel data!
Sender 1
Sender 2
channel sums together transmissions by sender 1 and 2
(provided the codes for different
senders are orthogonal)
M=8 (# bits)
Encoded data in slot 1:
-1*(+1,+1,+1,-1,+1,-1,-1,-1)
+ 1*(+1,-1,+1,+1,+1,-1,+1,+1)
= (0,-2,0,2,0,0,2,2)
Decoded data in slot 1 for Sender 1:
=(1/8)*(0*1+(-2)*1+0*1+2*(-1)
+0*1+0*(-1)+2*(-1)+2*(-1))
=(1/8)*(-8)=-1
IMPORTANT

## Slide 48: CDMA: two-sender interference
Orthogonal codes:
  Sender 1 Code: : (+1,+1,+1,-1,+1,-1,-1,-1)
  Sender 2 Code: (+1,-1,+1,+1,+1,-1,+1,+1)
  The two codes are orthogonal since their inner product is 0:
  (+1,+1,+1,-1,+1,-1,-1,-1) (+1,-1,+1,+1,+1,-1,+1,+1)
  =1*1+1*(-1)+1*1+(-1)*1 +1*1+(-1)*(-1)+(-1)*1+(-1)*1
  =0
Encoded data in slot 1 is sum of encoded -1 for Sender 1 and encoded 1 for Sender 2:
  -1*(+1,+1,+1,-1,+1,-1,-1,-1) + 1*(+1,-1,+1,+1,+1,-1,+1,+1)
  = (0,-2,0,2,0,0,2,2)
Decoded data for Sender 1 in slot 1 is :
  = (1/8)*(0,-2,0,2,0,0,2,2) (+1,+1,+1,-1,+1,-1,-1,-1)
  =(1/8)*(0*1+(-2)*1+0*1+2*(-1) +0*1+0*(-1)+2*(-1)+2*(-1))
  =(1/8)*(-8)
  =-1
Decoded data for Sender 2 in slot 1 is :
  = (1/8)*(0,-2,0,2,0,0,2,2) (+1,-1,+1,+1,+1,-1,+1,+1)
  =(1/8)*(0*1+(-2)*(-1)+0*1+2*1+0*1+0*(-1)+2*1+2*1)
  =(1/8)*8
  =1
IMPORTANT

## Slide 49: CDMA: two-sender interference: Sender 1
Decoded data for Sender 1 in slot 1 is
=(1/8)*((-1)*(+1,+1,+1,-1,+1,-1,-1,-1) +(+1)*(+1,-1,+1,+1,+1,-1,+1,+1)) (+1,+1,+1,-1,+1,-1,-1,-1))
=(1/8)*((-1)*(+1,+1,+1,-1,+1,-1,-1,-1) (+1,+1,+1,-1,1,-1,-1,-1) + (1/8)*(+1)*(+1,-1,+1,+1,+1,-1,+1,+1) (+1,+1,+1,-1,+1,-1,-1,-1))
(First term: Sender 1 Code’s inner product with itself is sum of M 1’s, M=8 is its dimension. Second term: Sender 1 Code’s inner product with Sender 2 Code equals 0, since the codes for different senders are orthogonal)
= (1/8)*(-1*(1+1+1+1+1+1+1+1) + 1*(1*1+1*(-1)+1*1+(-1)*1 +1*1+(-1)*(-1)+(-1)*1+(-1)*1))
= (1/8)*(-1*8+(+1)*0)
= -1
IMPORTANT

## Slide 50: CDMA: two-sender interference: Sender 2
Decoded data for Sender 2 in slot 1 is
=(1/8)*((-1)*(+1,+1,+1,-1,+1,-1,-1,-1) + 1*(+1,-1,+1,+1,+1,-1,+1,+1)) (+1,-1,+1,+1,+1,-1,+1,+1)
=(1/8)*((-1)*(+1,+1,+1,-1,+1,-1,-1,-1) (+1,-1,+1,+1,+1,-1,+1,+1) + (1/8)*1*(+1,-1,+1,+1,+1,-1,+1,+1) (+1,-1,+1,+1,+1,-1,+1,+1))
(First term: Sender 1 Code’s inner product with Sender 2 Code equals 0, since the codes for different senders are orthogonal. Second term: Sender 2 Code’s inner product with itself is sum of M 1’s, M=8 is its dimension.)
= (1/8)*(-1*0 + 1*(1*1+(-1)*(-1)+1*1+1*1+1*1+(-1)*(-1) +1*1+1*1))
= (1/8)*(-1*0 + 1*8)
= +1
IMPORTANT

## Slide 51: Quiz 1 CDMA
Q1: Consider the codes for two senders: Sender 1 Code: (+1,-1,-1,-1,+1,-1,-1,-1), Sender 2 Code: (+1,-1,+1,-1,+1,-1,+1,-1). Are they orthogonal?
A: Inner product (+1,-1,-1,-1,+1,-1,-1,-1) (+1,-1,+1,-1,+1,-1,+1,-1) = 4, so not orthogonal
Q2: Consider the codes for two senders: Sender 1 Code: (+1,-1,+1,-1,+1,-1,-1,-1), Sender 2 Code: (+1,+1,+1,+1,+1,+1,+1,-1). Are they orthogonal?
A: inner product (+1,-1,+1,-1,+1,-1,-1,-1)(+1,+1,+1,+1,+1,+1,+1,-1) = 0, so they are orthogonal
Q3: With the codes in Q2, suppose Sender 1 sends data bit 1 and Sender 2 sends data bit -1 simultaneously, compute the encoded data.
A: (+1)*(+1,-1,+1,-1,+1,-1,-1,-1) + (-1)*(+1,+1,+1,+1,+1,+1,+1,-1)=(0,-2,0,-2,0,-2,-2,0)
Q4: Compute the decoded data bit for Sender 1 and decoded data bit Sender 2.
A: Decoded bit for Sender 1: (1/8)*(0,-2,0,-2,0,-2,-2,0)(+1,-1,+1,-1,+1,-1,-1,-1) = +1
Decoded bit for Sender 2: (1/8)*(0,-2,0,-2,0,-2,-2,0)(+1,+1,+1,+1,+1,+1,+1,-1) = -1
IMPORTANT

## Slide 52: Quiz 2 CDMA
Q: A CDMA receiver receives the following encoded data:
(-1 +1 -3 +1 -1 -3 +1 +1).
Assuming the following codes used by four sending stations (they are pairwise orthogonal to each other),
  A=(-1,-1,-1,+1,+1,-1,+1,+1)
  B=(-1,-1,+1,-1,+1,+1,+1,-1)
  C=(-1,+1,-1,+1,+1,+1,-1,-1)
  D=(-1,+1,-1,-1,-1,-1,+1,-1)
which stations transmitted, and which bits did each one send?
A: Compute the normalized inner products with each code:
  A’s data:(1/8)*(-1 +1 -3 +1 -1 -3 +1 +1) (-1,-1,-1,+1,+1,-1,+1,+1) = 1
  B’s data:(1/8)*(-1 +1 -3 +1 -1 -3 +1 +1) (-1-1+1-1+1+1+1-1) =-1
  C’s data:(1/8)*(-1 +1 -3 +1 -1 -3 +1 +1) (-1+1-1+1+1+1-1-1) =0
  D’s data:(1/8)* (-1 +1 -3 +1 -1 -3 +1 +1) (-1-1-1-1-1-1-1-1) = 1
Stations A, B, and D transmitted bits 1, -1, 1 respectively while station C did not transmit.
  Transmitted bits 1, -1, 1 correspond to application bits 1, 0, 1
IMPORTANT

## Slide 53: Summary
Wireless is different!
Shared medium by default
Attenuation due to distance and obstacles
Rapidly shifting environments
Collision detection is different
Use MACA instead of CSMA for collision detection at receivers.
Modulation reference:
https://www.taitradioacademy.com/topic/how-does-modulation-work-1-1/